## Slide 1
An intuitive gNMI CLI and
a feature-rich telemetry collector*
Roman Dodin
ntdvps
* Fully open source

## Slide 4
June 27, 2018, NANOG 73
https://youtu.be/McNm_WfQTHw
SNMP is
💀

## Slide 5
From Monitoring to Telemetry
Network size
High data definition
CPU-friendly
Push-based mode
TCP
Reliable delivery
Notes: Explain a shift happening in modern networks where network monitoring is transitioning from monitoring to telemetry stacks
A few distinctive and ubiquitous change patterns can be seen in modern networks which take traditional monitoring technologies hostage
  Growth in network size poses a critical impact to monitoring stacks that were designed for use on networks with a much smaller scale
  Due to an increased application scope of a monitoring stack (alerting, closed-loop automation) we demand a finer grained data to be collected
  An immediate and unpredicted mode that SNMP operates in puts CPU under a lot of stress. Streaming telemetry instead uses a push based, subscription initiated mode that allows a CPU to make optimizations to the streamed out data
  Finally, as we approach closed-loop automation systems based on data injected via streaming telemetry we require a reliable transport such as TCP to deliver it.

## Slide 6
gRPC Network Management Interface
Network Management
Streaming Telemetry
The intention is that a single gRPC service definition can cover both configuration and telemetry

## Slide 7
gNMI wasn’t the only option, wasn’t it?
RFC 8641 (sept 2019) Subscription to YANG Notifications for Datastore Updates (aka YANG Push)
Has all there is, but lacks adoption.
RFC 8641
RFC 8641
gNMI
SNMP

## Slide 8
What is gNMIc to gNMI?
Command Line Interface for gNMI
Highly Available and flexible collector
Go API for gNMI with a human touch

## Slide 9
Rich CLI to explore and test gNMI enabled targets
RPC commands
Utility commands
Capabilities
Get
Set
Subscribe
Prompt
Generate
Diff

## Slide 10
Configure the way you want
CLI flags
gnmic [global-flags] [command] [local-flags]
gnmic --address 10.0.0.1:57400 \
--username admin --password admin\
--skip-verify \
get --path /interfaces/interface[name=mgmt0]

## Slide 11
Configure the way you want
CLI flags
Env variables
export GNMIC_ADDRESS=10.0.0.1:57400
export GNMIC_USERNAME=admin
export GNMIC_PASSWORD=admin
export GNMIC_SKIP_VERIFY=true
gnmic [global-flags] [command] [local-flags]

## Slide 12
Configure the way you want
CLI flags
Env variables
File configuration
$ cat .gnmic.yaml
address: router1
username: admin
password: admin
insecure: true
encoding: json_ietf
get-path:
- /interfaces/interface[name=mgmt0]
$ gnmic --config .gnmic.yaml get

## Slide 13
Get / Set / Subscribe from the comfort of your terminal
Get
gnmic –a leaf1 \
–u admin –p admin \
--encoding json_ietf \
get \
--path /system/state/hostname

## Slide 14
Get / Set / Subscribe from the comfort of your terminal
Set
gnmic –a target.address \
set \
--update-path "/interface[name=ethernet-1/1]/admin-state" \
--update-value "enable" \
--encoding json_ietf

## Slide 15
Get / Set / Subscribe from the comfort of your terminal
Subscribe
gnmic –a target.address \
subscribe \
--path "/interface[name=ethernet-1/1]/statistics/in-octets" \
--encoding json_ietf

## Slide 16
A performant and highly available gNMI collector

## Slide 17
Defining targets
targets:
leaf1:
...: ...
subscriptions:
- ...
outputs:
- ...
Define per target connection options
Bind specific subscriptions
Bind specific outputs
gnmic.yaml
subscriptions: ...
outputs: ...

## Slide 18
Collector outputs
gNMI
Database
Message queue
Terminal/File
Targets
Collector
Outputs

## Slide 19
Processors
Data manipulation
  Type conversion
  Grouping
  Message enrichment
Filtering (allow/deny lists)
Trigger (gNMI, HTTP, script, template)
outputs:
output1:
event-processors:
- proc1
- proc2
scrape
Collected telemetry metric
gNMI
processing pipeline
Changed/processed metric
Processor
Notes: JQ and starlark
Topology clone example

## Slide 20
High availability
Scaling
Automatic cluster formation
Automatic target redistribution
Clustering: The more the merrier
gNMIc cluster

## Slide 21
Deployment examples
deployment examples

## Slide 22
/
openconfig/gnmic
Nokia donated gNMIc to Openconfig

## Slide 23
Sounds interesting, what’s next?
1 Explore gnmic.openconfig.net documentation portal
2 Try out the deployment examples
3 Missing feature, a problem, a nice idea? Reach out to us via Github Issues/Discussions
4 Give gNMIc repo a ⭐ and grab a sticker