## Slide 1: High-performance Synchronization Transport Challenges and Solutions
Martin Wahlsten Senior Director Product Line Management
2023-03-08
DKNOG13

## Slide 2: What is driving the need for time?
Telecom: Software controlled virtual antennas
High accuracy data aquisition and timestamping
Audit based applications (who did what when?)
Media distribution
Mobile networks
Power and utility networks
Industrial Automation
TaaS (Time as a service)

## Slide 3: What is time in the transport network?
SyncE G.8262 and G.8262.1
Target of 1588v2
*Hardware timestamped systems dows not utilize optional follow-up message
The obvious question? Why are we spending 30 minutes of our lives on this topic today? Problems seems solved to me?

## Slide 4: Example Causes of Asymmetry in Optical Transport
Class C T-BC
Ethernet Switch
Fiber
Coherent Optics
OTN Mapping
Optical Devices
Coherent Optics
Optical Devices
OTN Mapping
Class C T-BC
Ethernet Switch
Fixed cTE components
Random cTE components
Random cTE components
Contributor | Fiber | Optical Devices (Dispersion Comp, OA/ILA, ROADM) | Coherent Optics | OTN Mapping | IP Routing and Ethernet Switching
Source | Asymmetry in fiber lengths, jumper cables, etc. 2.5 ns/m (vs 5 ns/m latency) | Random asymmetry in fiber lengths used in each direction | FIFO buffers in DSP Varies on restarts | Deep FIFO buffers in OTN mapping Varies on restarts | Traffic/buffering asymmetry and timestamping inaccuracy
Impact | Large but static | Very large but static | Varying and random | Large and random | Tight requirements to control impact
Range | Fixed cTE of ±5 to 1000+ ns | Fixed cTE of ±5 to 20,000 ns | Random cTE of ±20 to 130 ns on restart | Random cTE of ±20 to 1000 ns on restart | Class A/B/C specifications Max(TE) of 30 to 100 ns cTE of 10 to 50 ns dTE (low-pass filtered) of 10 to 40 ns

## Slide 5: 5G Drives Vast Majority of High-accuracy Synchronization Requirements
ePRT/PRTC
15 ns - 100 ns
Transport Network 1000 ns
eCPRI Transport
60 ns - 190 ns
eREC
eRE
TDD/LTE-A and 5G macro phase services traceable to UTC
Inter antenna relative phase alignment
Network Budget
Max|TE|
4G
5G
4G
5G
CPRI
eCPRI
eCPRI
CPRI
CU
CU
MEC
MEC
MEC
PRTC/T-GM
ITU-T G.8273.2 PTP T-BC Class C
Fronthaul
Network
Midhaul
Network
ITU-T G.8275.1 Full Onpath Support
ITU-T G.8262.1 eEEC Synchronous Ethernet
3GPP TS 38.104 Time Alignment Error
ITU-T G.8271.1 Network Limits
DU
BBU
IP/MPLS Access DWDM
Fronthaul
Midhaul and Backhaul
5G
Ethernet
ITU-T G.8273.2 PTP T-BC Class B/C
ITU-T G.8275.1 Full Onpath Support
ITU-T G.8262.1 eEEC Synchronous Ethernet
Backhaul
Network
IP/MPLS Metro DWDM
IP/MPLS Core DWDM
T-TSC
T-TSC
IP Router or Ethernet Switch with inbuilt T-BC

## Slide 6: 1588 clock types
PTP
UDP
IP
MAC
Phy
PTP
UDP
IP
MAC
Phy
Master
Boundary clock
Boundary Clock
PTP
UDP
IP
MAC
Phy
MAC
Phy
Master
Transparent Clock
Transparent Clock
MAC
Phy
PTP
UDP
IP
MAC
Phy
Boundary clock
Boundary clocks interacts on the application layer
A Transparent clock justifies for resident time from Rx to Tx utilizing hardware timestamping into the 1588 frames
Type | Max time error | Configuration
Class A | 100 ns | Significant
Class B | 70 ns | Significant
Class C | 10 ns | Significant
Class D | 5 ns | Significant
Type | Resolution | Configuration
EMXP/IIE | 8 ns | Trivial
XH800 | 2 ns | Trivial
Boundary clocks helps scale 1588 domains by hiding clients befind BCs
Transparent clock resolution does not define E2E max time error, that is still also a property of the boundary clock and the PTP servos.

## Slide 7: Viable strategies for building cost efficient national synchronization distribution

## Slide 8: Viable strategy #1 choose good electronics
Card | Function | Client | cTE (ns) | dTE LF (ns) | Phase sync
FXP400GOTN | Dual 2x 100/200G OTN Flexponder | 100G | 20 | 0 | OK
FXP400G-E | 4x 100 / 400G OTN Flexponder | 100G/ 400G | 12 | 0 | OK
MXP200GOTN | 100/200G OTN Muxponder. | 10G / 100G | 670 | 0 | No
EMXP440/III | 10G and 100G/200G Packet Optical Muxponder | 10G / 100G | 37 | <5 | OK
XH800 | 10G/25G/100G/200G Packet Optical Transport Switch | 10G, 25G / 100G | 28 | <5 | OK
TPHEX10GOTN | 6x 10G OTN Transponder | 10G | 372 | <5 | No
FHAU/I | 6x10G iWDM Flexponder | 10G | 10 | 0 | OK
TPMRHEX-L/16G | 6x MultiRate Lite Transponder | 10G, GbE | 0 | 0 | OK
Some cards use highly optimized Infinera technology that does Ethernet and ethernet only. Laserfocus on sync performance, both SyncE and PTP.
Other use OTN technology built with merchant silicon offering a wide variety of client formats and services (Ethernet, SDH, Fibre Channel, etc).
Deep service mapping OTN cards are unsuitable for inline transport of 5G synchronization transport in mobile networks. Optimized technology, such as the OTN Flexponder, Fronthaul Flexponder or EMXPs works just fine.
Summary table of some XTM cards and Time Errors

## Slide 9: The importance of understanding the full synch stack
1588-BC
1588-BC
Transport System
100G Coherent
Transport System
Customer wanted to know why there was line re-synch events (glitches) when 1588 protocol was starting up and was accuring phase/synch?

## Slide 10: Viable strategy #2 Optimize linesystem or bypass assymetries using OTC
Utilize single fiber operation to eliminate errors from line system assymetries
Utilize direct-detect optics (GbE/FE/10G/HD-CWDM) optics to eliminate processing time error from a coherent dataplane
3rd party T-BC or T-TC can be utilized with INFN XTM linesystem
Time Error margin 7 hops
Excellent e2e cTE performance 11 ns, 1 week Test Case

## Slide 11: Building High-Performance Optical Timing Channels
SYNC LAYER CONSIDERATIONS:
High performance boundary clock operation
vPRTC / Timing cloud architecture
Demanding performance/feature requirements:
  Class D cTE within ± 5 ns, max. |TE| <5 ns
  Hop-by-hop local clock recovery, OCXO holdover
  Resiliency mechanisms
  GNSS/Grandmaster options
Supporting optical layer interoperability:
  BiDi single fiber working optics
  Large (up to 6) number of degrees/directions
OPTICAL LAYER CONSIDERATIONS:
Fiber topology and resiliency – Ring, Linear, Tree, Mesh
Analogue domain – many factors to balance:
  Managing fiber effects – asymmetry, non-linear effects, dispersion etc.
  Optical add/drop – ROADM / Fixed add/drop
  Amplification options – EDFA / Raman
  Bandwidth – C Band / C+L Bands
Optical Timing Channel Toolkit:
  Timing channel options – O/E/L-band
  Sync/Retiming options – High performance T-BC, Integrated T-BC (Router) or optical 3R
Optical Layer Foundation
Notes: Key messages:
  Infinera way to operationalize disaggregation on complex nodes

## Slide 12: 1588 PTP High Accuracy Clocking with XH800
Optical Timing Channel overlay
XH800 T-BC uses SyncE assisted high performance functionality, performing better than T-BC Class C requirements.
XH800 T-BC has Stratum 3E holdover performance
Full implementation of G.8275.1 PTP Telecom Profile
  1 ns timestamping T-TC function.
XH800 supports the enhanced EEC requirements
Fiber asymmetry compensation
XTM/XH800 can use single fiber CWDM Optical Timing Channel for time sync, eliminating static errors
T-BC
ITU-T G.8273.2 Timing characteristics of telecom boundary clocks
PTP T-BC Class C
ITU-T G.8275.1 PTP Telecom Profile for phase/time synchronization with full timing support from the network
ITU-T G.8262.1 Enhanced EEC Synchronous Ethernet
and DAA requirements
Fiber and network asymmetry
TRX100176/01U
1588-TC performance utilizing 2ns hardware time-stamping for suitable for transport of even Class-D clocks

## Slide 13: Performance performance performance
Ideal TC-performance
Ideal BC-performance
Ideal TC-output
Specifications are over lifetime, temperature, supported operational conditions

## Slide 14: Sychronization Distribution Strategies
In-band Delivery (XTM Series)
Optical Timing Channel (XTM/OTC2.0)
In-band delivery of synchronization
Transponder synchronization performance
Coherent synchronization performance
High-performance PTP 1588 and SyncE delivery
Hybrid Sync Distribution
Hybrid use of in-band and OTC mechanisms
Interoperable and interchangeable
All high-performance 1588 PTP, not proprietary
Use the appropriate solution for the best fit
  In-band delivery perfect for metro-access
  OTC widely used as core distribution
T-GM
T-GM
T-GM
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC/3R
T-BC/3R
T-BC/3R
Out-of-band delivery of synchronization
Single-fiber HD-CWDM and O/E/L-band overlay
Very high-performance PTP 1588 and SyncE
OTC network elements:
  OTC 2.0 T-BC Class D or XH800 Class C boundary clocks
  High accuracy T-TC
  Optical 3R regeneration via HEX-LIGHT card

## Slide 15: Creating an OTC-enabled vPRTC/Timing Cloud
OTC-ENABLED vPRTC:
Provides GNSS-like omnipresent timing, overcoming GNSS security/reliability/accessibility issues
Uses secure and reliable optical network to deliver highly-accurate timing/synchronization:
  Predictable, traceability to UTC and PRC
  Reliable and secure
  Highly-accurate
Flexible and independent
Every DWDM node capable of delivering timing/synchronization
Preserves timing budget for access/aggregation networks
Simplifies timing/synchronization planning and ongoing operations
Range of 100 ns vPRTC (Timing Cloud) resilient timing service
Redundant GNSS spoofing hardened GM/ Cesium source
5G Fronthaul /Midhaul
Other timing critical applications (power distribution, scientific)
vPRTC (Timing Cloud) with every DWDM node capable of delivering timing/synchronization
56.6 km
39 km
48.3 km
54 km
72 km
13 km
9 km
9 km
16 km
6 km
10 km
24.3 km
58.2 km
53.3 km
56.2 km
54.5 km
53.6 km
81 km
65 km
60 km
35.3 km
38.1 km
50 km
71 km
53 km
44 km
51 km
58 km
72 km
60 km
36.2 km
53.7 km
100 ns
5G Fronthaul /Midhaul

## Slide 16: Takeaways
Key messages
Synchronization is not trivial and have a wide range of optimization points in cost/performace
Multilayer understanding is required to build a viable and good performant synch network
  Synch performance can be heavilly impacted by many factors
Recommendations
Work with people and suppliers that knows what they are doing in this space
Ask one question to much rather one to little

## Slide 17: Resources for further reading
INFINERA SYNC E-BOOK
(CLICK HERE)
SYNC BLOGS ON
INFINERA.COM
https://infinera.sharepoint.com/:f:/s/COR-RDPO/Eji2UW1E15NLv_IB_D1XxycB01moob2fwFhcmkdpHO5K9A?e=dvJVF0
EVENTS (ITSF & WSTS)
WEBINARS