## Slide 1: SCION: SECURE PATH-AWARE INTERNET ROUTING
Kevin Meynell, SCION Association <kme@scion.org> APRICOT 2024, February 2024

## Slide 2: WHAT IS ROUTING AND WHY IS IT NEEDED?
  Routing is needed to get packets from one destination to another (unless on the same subnet)
  Routers are devices that discover other connected networks and forward packets to them
  Each network is connected to the rest of Internet with a router
  Packets are forwarded by routers to other routers (hops) or final destination, based on IP prefixes
  Routers use Border Gateway Protocol (BGP) to exchange “reachability information” - networks they know how to reach
  Routers build a routing table (i.e. “road map”) to pick the best route when sending packets
  Networks can control what to send to and accept from directly connected (‘next hop’) networks, but generally have no control over how packets are routed across the Internet – i.e. the path
Internet, a global system of interconnected systems using TCP/IP protocols

## Slide 3: THE GLOBAL ROUTING SYSTEM
as of 24 January 2024
75,454 networks known as Autonomous Systems connected to the Internet, each using a unique Autonomous System Number (ASN) for identification
943,556 advertised IP prefixes (routes)
Many possible paths across the Internet

## Slide 4: THE ROUTING PROBLEM
Border Gateway Protocol (BGP): the Internet routing protocol
The Border Gateway Protocol (BGP) used by the Internet routing system is inherently based on unverified trust between networks
No built-in validation that route advertisements are legitimate
Any network can announce any ASN or IP prefix
Any network can claim to be another network
Sending and receiving networks cannot decide the path that intermediate routers direct their traffic across the Internet

## Slide 5: WHY IS THIS A PROBLEM?
EVENT | EXPLANATION | REPERCUSSIONS | EXAMPLE
ROUTE LEAK | Usually accidental but sometimes malicious redirection of traffic through an unintended path. A network operator with multiple links announces to an upstream provider that has a route to a destination through another link. | Traffic is delayed or never delivered, with the intermediate network(s) carries unintended traffic. Can be used for MITM including traffic inspection and/or modification. | In Jun 2019, Verizon accepted incorrect routes from DQE Communications that diverted traffic destined for Cloudflare, Facebook & Amazon through small ISP.
ROUTE OR PREFIX HIJACKING | A network operator or attacker impersonates another network operator by falsely announcing ownership of IP prefixes and/or ASNs. Re-routes traffic by offering a shorter or more specific path for malicious or censorship reasons. | Traffic is forwarded to the wrong destination. Can be used for Denial-of-Service attacks, traffic interception or network masquerading. | Feb 2022 – KLAYswap Cryptocurrency hijack Apr 2018 - Amazon Route 53 hijack Feb 2008 - YouTube hijack
DATA SOVEREIGNTY BREACHES | BGP routing can, and often does, send traffic across geopolitical boundaries. | Can breach national and supra-national (e.g. GDPR) data protection legislation. | May 2023 – Australian healthcare data transferred through another country.
Some info @ a glance

## Slide 6: ROUTING PROBLEMS 101
Data sovereignty
Different countries have different regulations regarding transfer of sensitive data across geopolitical borders.
Routing can send traffic through different jurisdictions, thereby making regulatory compliance complex.

## Slide 7: HOW IS THIS BEING ADDRESSED?
EVENT | EXPLANATION | LIMITATIONS
RPKI & ROV Resource Public Key Infrastructure & Route Origin Validation | ROAs (Route Origin Authorisations) provide cryptographic assertions of IP prefix ownership and which ASNs are allowed to originate them. Routers can validate ROAs and generate appropriate route filters. | Requires widespread deployment to be effective (less than 50% of IP prefixes are signed in 2024) Few network operators currently use ROV (5%). Only does origin validation and does not validate paths through the Internet.
BGPSEC BGP Security | Builds on RPKI to provide cryptographic assertions that every router (hop) en-route to a destination has authorized the advertisement of that route. Prevents unauthorised insertion of ASNs into a path to circumvent RPKI. | Needs to be explicitly supported by all routers along a path to achieve full benefits. Computationally intensive and introduces significant delays in route convergence. Explicit path selection is not possible. Almost no deployment.
ASPA Autonomous System Provider Authorization | ASPA objects are similar to ROAs, but allow ASNs to authorize other ASNs to carry their traffic through the Internet. Works out-of-band so doesn’t need to be deployed on all routers. | Developmental stop-gap technology and not yet an Internet standard. Does not provide assurances that traffic will actually follow validated paths.
SCION | Inter-domain routing architecture offering secure path awareness and selection. | Needs to be supported by border routers.
Some info @ a glance

## Slide 8: WHAT IS SCION?
SCION is an inter-domain path-aware architecture
Internet-based secure and reliable communication for critical infrastructure ecosystems (e.g. financial services, power utilities, emergency services, government, …)
Office
IoT
Home
office
Cloud
Data center
Bank
INTER-DOMAIN MULTIPATH ROUTING:
Fast path failover (can switch to backup path in ~RTT)
Multi-operator
PATH CONTROL:
Source endpoints can select AS path (included in packet header)
PATHS ARE AUTHENTICATED AT DISCOVERY
AND VERIFIED AT FORWARDING:
Higher assurance that packets will follow certain path
Hijacking prevention
Geofencing

## Slide 9: TRUST-ENHANCED NETWORKING
Trust model is based on Isolation Domains (ISDs)
  An ISD is a logical grouping of ASes sharing a uniform trust environment (e.g. a common jurisdiction).
  Each ISD is administered by one or more ASes via a voting mechanism. These are known as core ASes and form the ISD core.
  Every ISD has its own trust root specified in the Trust Root Configuration (a collection of X.509 certificates with ISD information) - negotiated by the ISD core according to its own trust policy. Not reliant on third-party CAs.
  The CAs in an ISD can only create certificates for ASes in their respective ISD.
  This is the main building block of SCION
0
Q
R
C
D
G
E
H
N
I
J
P
O
K
F
L
S
A
B
M
Core
Core
Core
TRC
TRC
TRC
Notes: The building block of SCION

## Slide 10: HOW IT WORKS
SCION core components in a nutshell
DATA PLANE - PACKET FORWARDING
Combine path segments into end-to-end path (ISD-AS level)
Packets contain end-to-end ISD-AS path
Forward packet based on end-to-end path, agnostic of end-host address
CONTROL PLANE – INTER-DOMAIN ROUTING
Discover valid inter-domain paths
Construct and disseminate path segments
Routing is based on <ISD>-<AS> tuple as “locator”
Intra-AS communication reuses existing data plane and routing (e.g. IPv6/IPv4)
CONTROL PLANE PKI (CP-PKI) - AUTHENTICATION
Authenticate path information
Used by control plane
Unique ISD trust model – scalability of trust and routing
0
Q
R
D
G
E
H
N
O
K
L
B
Core
Core
Core
AS
Isolation Domain (ISD):
Grouping of Autonomous Systems (AS)
Each ISD has its own trust root
For routing protocol scalability
F➔C➔A
A➔I➔J➔M
M➔P➔S
Packet P1
Payload
Packet from AS F to AS S
A
I
J
C
P
M
F
S
ISD
ISD
ISD

## Slide 11: DEPLOYMENT MODEL
Border router
C
SCION AS
SCION routers are set up at the borders of an AS
Border routers peer with other SCION-enabled networks and collect customer traffic
Control services discover and map network paths
No change to the internal network infrastructure of a network operator needed.
Endpoints run a SCION stack
Legacy endpoints can use SCION gateways
Control Services
Internal router
AS
C

## Slide 12: SCION CONTROL PLANE
A look at how it works
0
Q
R
C
D
G
E
H
N
I
J
P
O
K
F
L
S
A
B
M
Core
Core
Core
ISD
ISD
ISD
Simulations on CAIDA AS topology (2k core ASes, 7k ASes in single ISD, 12k ASes total) suggest similar Core beaconing messaging overhead to BGPsec, and 1-2 orders of magnitude better for Intra-ISD beaconing.
Control plane mechanisms:
Grouping ASes into ISDs - isolates AS control planes and reduces communications overhead
AS-level routing - establishes paths on AS basis instead of on prefix basis
Beaconing:
Path-segment Construction Beacons (PCBs) messages are used to build path segments and routing paths
Core beaconing algorithm is used between all core ASes
Intra-ISD beaconing algorithm used between core and leaf ASes
Endpoints look up path segments and combine them to form end-to-end paths.

## Slide 13: SCION SETUP
CONTROL SERVICES (PER AS)
Beacon server – generate, receive and propagate path-segment construction beacons (PCBs) to construct path segments and routing paths.
Path server – store mappings of AS to path discovered during beaconing
Certificate server – cache copies of TRCs retrieved from ISD core, AS certificates and key management for inter-AS communication
Border routers – SCION packet forwarding to next SCION border router or destination host within the AS
SIMPLER, CHEAPER ROUTERS
SCION border routers only forward traffic and do not need to undertake control plane operations
SCION border routers do not need to maintain inter-domain forwarding tables so do not require large and expensive TCAMs.
One AES operation per packet for Message Authentication Code verification
Paths can be used as soon as they are disseminated.

## Slide 14: SCION BENEFIT: FAST MULTI-PATH DISCOVERY & FAILOVER
BGP generally selects routes based on ‘lowest cost’ regardless of whether these are in practice the most optimal or they meet particular requirements.
With SCION, Leaf ASes only receive and do not forward any beacons. Only core ASes initiate beacons.
Beaconing does not rely on iterative convergence nor forwarding table updates, allowing rapid path exploration within ISDs.
The control services discover path segments and assemble these into available paths.
Tests show path failover to be within 1-2 seconds.
Applications can choose paths based on optimal characteristics or other parameters, and can also use multiple paths simultaneously.
Unique differentiator

## Slide 15: SCION BENEFIT: PATH VALIDATION
Experimental extensions
PROPERTY | APPROACH | COMPONENT
PATH AUTHORIZATION (HOP-BY-HOP) | Information at each hop is authenticated with a MAC (Message Authentication Code), checked by border routers at forwarding. Each AS only forwards traffic on paths that are explicitly authorized by the AS. | Standard SCION
PROOF OF FORWARDING | EPIC adds short per-packet MACs at each SCION hop. Source authentication and path validation are enabled by the additional use of efficiently derivable symmetric keys. | EPIC extension, L3 [1]
TRUST-ENHANCED NETWORKING | Packet headers are extended with policies telling border routers which intra-AS path to forward the packet, so that endpoints can select routers/ASes with specific path policies. Inter-domain paths are this way mapped to policy-compliant intra-domains paths. Per-AS attestation done by a third part. | FABIRD extension [2]
Legner, Markus, et al. "EPIC: every packet is checked in the data plane of a Path-Aware Internet." 29th USENIX Security Symposium (USENIX Security 2020).
Krähenbühl, C., Wyss, M., Basin, D., Lenders, V., Perrig, A. and Strohmeier, M., 2023. FABRID: Flexible Attestation-Based Routing for Inter-Domain Networks. (USENIX Security ‘23)

## Slide 16: REAL-WORLD DEPLOYMENT: THE SECURE SWISS FINANCE NETWORK
SOME FACTS:
300+ finance institutions
Network handling ~200 Billion CHF/day
Migration to SCION-based SSFN ongoing until September 2024
Swiss inter-banking network, handling money transfers between banks and other critical real-time financial services, operated by SIX, the Swiss Financial Infrastructure operator.
Reasons for using SCION:
Enforceable governance thanks to SCION’s trust concept
Performance-based routing & fast failover
Geofencing
Multi-ISP
https://www.six-group.com/en/products-services/banking-services/ssfn.html

## Slide 17: SSFN DEPLOYMENT EXPERIENCES
WHY WAS SCION ADOPTED?
SIX clients previously used Finance IPNet or point-to-point connections. Finance IPNet was reaching end-of-life.
IPNet did not limit connections to the rest of the Internet (e.g. no route controls) and offered limited protection against cyber risks.
Point-to-point connections lacked flexibility and had single points of failure.
Lacked strong governance and geofencing.
LESSONS LEARNED
Establishment of an ISD requires the creation of admission criteria, process documentation, and legal agreements.
Initial establishment of ISDs requires key-signing ceremony involving voting ASes.
Manual checks are needed when onboarding candidate ASes to ensure they meet admission criteria.
Building the PKI and management integration of the services was challenging (although SSFN offers managed service).
Certificate revocation not possible, although they expire within 72 hours.
SCION products are still relatively new and not all features are implemented yet.
Inter-ISD path control is currently limited.
The community and sources of expertise are currently limited.
Practical experience has been that path failover and fallback occurs within a few seconds.

## Slide 18: DEPLOYMENT BEYOND FINANCE
HEALTHCARE
EDUCATION
POWER
The HIN Trust Circle adopts SCION to interconnect hundreds of hospitals and thousands of doctors.
The SCION Education, Research & Academic Network connects campuses with path-aware high performance SCION connectivity.
In 2023, the Association of Swiss Electricity Companies explores SCION to connect electricity market players.
Doctors
Insurances
Rescue
Patients
Pharmacies
Labs
Administration
Hospitals

## Slide 19: COMMERCIAL & OPEN-SOURCE IMPLEMENTATIONS
If you’re interested in deploying SCION, there are currently two options:
Commercial
Open Source
Other implementations under development: P4, Rust, OpenWRT
SCION Association formed by deployers and early adopters to support open source development, standardization, and community involvement.

## Slide 20: INTERNET ENGINEERING TASK FORCE
Standardisation is important for interoperability and to encourage other implementations
SCION components and functionality currently being documented through PANRG (an IRTF Working Group)
Discussions with other IETF Working Groups
Independent Submission Stream
Hackathon @ IETF 118: Control Plane RPC over HTTP/3
Current Internet Drafts:
SCION Overview draft-dekater-panrg-scion-overview
SCION Components draft-rustignoli-panrg-scion-components
SCION PKI draft-dekater-scion-pki
SCION Control Plane draft-dekater-scion-controlplane
SCION Data Plane draft-dekater-scion-dataplane

## Slide 21: ABOUT THE SCION ASSOCIATION
COMMUNITY
We raise awareness on the benefits of SCION and cultivate its community, and support implementors and deployers with marketing.
STANDARDIZATION
We create the specifications to implement SCION, with the goal of making it a global Internet standard
OPEN SOURCE
We coordinate and maintain a SCION implementation for research, development, and experimental deployments.
Promoting openness and collaboration to unlock the full potential of SCION
Non-profit association established in 2022
Open for membership to entities interested in SCION
https://www.scion.org

## Slide 22: SCION TODAY
A growing ecosystem
Vendors, Integrators
Research
Users
ISPs

## Slide 23: THANK YOU!
More information:
The Complete Guide to SCION
Springer Verlag, 2022
SCION Association: https://www.scion.org
Reference & Developer Docs: https://docs.scion.org/
Research: https://scion-architecture.net
Vendor: https://www.anapaya.net/resources
Latest Release: https://github.com/scionproto/scion/releases/