## Slide 1: SRv6 uSID Introduction DKNOG
Jakub Horn
Principal Technical Marketing Engineer
Mar 2024

## Slide 2
Understanding Today’s Service Creation
Metro Network Domain
Core Network Domain
Data Center Domain
Legacy Central Office
Access
Aggregation
Hardware Appliances
Limited Cross-domain Automation, Cumbersome Service Assurance
End-to-end service provisioning is lengthy and complex
Multiple network domains under different management teams
Manual operations
Heterogeneous underlay and overlay networks
Centralized Services Delivery
VNF
IP
MPLS
L2VPN
Ethernet
L3VPN
VXLAN
VNF
Complex E2E Quality of Service (QoS)
Notes: Let me walk you through how services are instantiated today. For that, we need to look at the network infrastructure from an End-to-End perspective.
Service Providers’ networks are composed of multiple domains – Access, Metro, Core and Data Center.
These domains are most of the time operated by different teams and are using different underlay and overlay protocols. Here are some examples of Underlay and Overlay protocols that are commonly used in these domains:
- Metro domain: Underlay – Ethernet / Overlay – L2VPN
- Core domain: Underlay – MPLS / Overlay – L3VPN
- Data Center domain: Underlay – IP / Overlay - VXLAN
As a consequence, cross-domain orchestration is complex and limited.
To deliver new services, Services Providers have made great usage of purpose-built HW appliances rolled out in Central Offices. This mode of operation is obviously not sustainable for the following reasons:
- It requires truck-roll and onsite installation resulting in OpEx increase
- Every HW appliance comes with its own management system and hence requires custom integration into OSS/BSS. Moreover, each of these HW appliances have their own lifecycle making the upgrade of the overall Central Office a tedious planning exercise.
To overcome these limitations, Service Providers have started to deliver new services from centralized Data Centers, leveraging compute infrastructure and VNFs. Straightforward Benefits are Time-To-Market and On-demand service instantiation.
Delivering services from centralized Data Centers comes with its own set of challenges though. This mode of operation requires to construct E2E connectivity across the network - from Central Offices up to Data Centers. This is actually a lengthy and complex task:
- As underlay and overlay protocols are different across network domains, protocol translations have to take place across domains. This brings complexity and sometimes requires network devices to maintain states hindering cloud scale scalability.
- These “stitching” operations are still largely manual and require coordination between operations teams
By and large, this creates a dichotomy between the on-demand service instantiation in Data Centers and the lengthy procedures required to update the network infrastructure to support those new services.

## Slide 3
SDN
Metro Network Domain
SDN
Core Network Domain
SDN
Data Center Domain
Aggregation
Homogenous Cross-domain Automation & Assurance
End-to-end service provisioning is simple
Multiple network domains under same management teams
Automated operations
Homogenous underlay and overlay networks
Centralized Services Delivery
Segment Routing
VPN L2/L3
SR-MPLS: SDN ready “Network as a Fabric” for Service Creation
Cloud Scale Networking
Central Office
Access
Compute
Leaf
Spine
VNF
VNF
VNF
VNF
SDN
Control

## Slide 4
SDN
Metro Network Domain
SDN
Core Network Domain
SDN
Data Center Domain
Aggregation
Homogenous Cross-domain Automation & Assurance
End-to-end service provisioning is integrated with NfV, SDN
Multiple network domains under same management teams
Automated operations
Integrated underlay and overlay networks (NfV)
Network as API (NfV)
Hyper Scale (5G)
Centralized Services Delivery
SRv6: SDN, NfV, 5G ready “Network as an API” for Service Creation
Cloud Scale Networking
Central Office
Access
Compute
Leaf
Spine
VNF
VNF
VNF
VNF
SDN
Control
Segment Routing v6 (transport, services and programmability)

## Slide 5: Content:
  uSID Technology
    SRv6 DataPlane
    SRv6 Network Programming
    SRv6 ISIS
    SRv6 BGP

## Slide 6
SRv6
IPv6 Segment Routing Header (SRH)

## Slide 7
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
SRv6
IPv6 Header
Destination IP address
6
4
143
Next header field:
  TCP, UDP, ICMP....
TCP data
source port
destination port
sequence number
acknowledgment number
hlen
reserved
code bits
window
checksum
urgent
options
TCP Header
  IPv4, IPv6
IPv6 Header
IP data
source IP address
ver
length
hl
tos
id
flags
fragment offset
ttl
protocol
header checksum
destination IP address
IP Packet
  IPv4, IPv6, L2
L2 Payload
destination MAC
ether type
destination MAC
source MAC
L2 Frame
source MAC

## Slide 8
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
SRv6
IPv6 Header
Destination IP address

## Slide 9
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
SRv6
IPv6 Header
Destination IP address
Next header field:
  TCP, UDP, ICMP....
TCP data
source port
destination port
sequence number
acknowledgment number
hlen
reserved
code bits
window
checksum
urgent
options
TCP Header
6

## Slide 10
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
IP data
source IP address
ver
length
hl
tos
id
flags
fragment offset
ttl
protocol
header checksum
destination IP address
SRv6
IPv6 Header
Destination IP address
Next header field:
  TCP, UDP, ICMP....
  IPv4, IPv6
IP Packet
4

## Slide 11
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
L2 Payload
destination MAC
ether type
destination MAC
source MAC
SRv6
IPv6 Header
Destination IP address
Next header field:
  TCP, UDP, ICMP....
  IPv4, IPv6, L2
L2 Frame
source MAC
143

## Slide 12
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
reserved
payload len
next header
authentication data
security parameters index
AH
SRv6
IPv6 Header
Destination IP address
Next header field:
  TCP, UDP, ICMP....
  IPv4, IPv6, L2
  Hop by Hop, Dest. Options, Fragmentation, Authentication Header …
sequence number
TCP data
source port
destination port
sequence number
acknowledgment number
hlen
reserved
code bits
window
checksum
urgent
options
TCP Header
51
6

## Slide 13
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
routing type
segments left
hdr ext len
next header
Routing Header
SRv6
IPv6 Header
Destination IP address
Next header field:
  TCP, UDP, ICMP....
  IPv4, IPv6, L2
  Hop by Hop, Dest. Options, Fragmentation, Authentication Header …
  Routing Header
    0 Source Route (deprecated)
    1 Nimrod (deprecated)
    2 Type 2 (RFC 6275)
    3 RPL (RFC 6554)
43

## Slide 14
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
flags
last entry
routing type
segments left
hdr ext len
next header
tag
SID[0]
SID[1]
SID[n-1]
Optional TLVs
SRH
RFC 2460
RFC 8754
SRv6
IPv6 Header
Destination IP address
Next header field:
  TCP, UDP, ICMP....
  IPv4, IPv6, L2
  Hop by Hop, Dest. Options, Fragmentation, Authentication Header …
  Routing Header
    0 Source Route (deprecated)
    1 Nimrod (deprecated)
    2 Type 2 (RFC 6275)
    3 RPL (RFC 6554)
    4 SRH (RFC 8754)
43
4

## Slide 15
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
flags
last entry
routing type
segments left
hdr ext len
next header
tag
SID[0]
SID[1]
SID[n-1]
Optional TLVs
SRH
SRH
Segment Routing Header
First Segment
  Pointer to very first SID
43
4

## Slide 16
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
flags
last entry
routing type
segments left
hdr ext len
next header
tag
SID[0]
SID[1]
SID[n-1]
Optional TLVs
SRH
43
4
ACTIVE SID
SRH
Segment Routing Header
First Segment
  Pointer to very first SID
Segments left
  Pointer to Active SID
  Active SID always in destination addr
ACTIVE SID
copy

## Slide 17: SID Structure -Locator
1111:2222:3333:4444:5555:6666:7777:8888
128 Bits Like IPv6 address but different semantics
Locator
Function

## Slide 18
SRv6 Full SID
S
R1
R2
R3
R4
R
2001:db8:0:1::/64
2001:db8:0:2::/64
2001:db8:0:3::/64
2001:db8:0:4::/64
SA:2001::1
DA:2001:db8:0:1:1::
NH:RH
Type:4(SRH)
NH:IPv4|SL:3
Segment List:
[0]:2001:db8:0:4:eeee::
[1]:2001:db8:0:3:48::
[2]:2001:db8:0:2:1::
[3]:2001:db8:0:1:1::
BGP:2001:db8:0:4:eeee::
SA:2001::1
DA:2001:db8:0:2:1::
NH:RH
Type:4(SRH)
NH:IPv4|SL:2
Segment List:
[0]:2001:db8:0:4:eeee::
[1]:2001:db8:0:3:48::
[2]:2001:db8:0:2:1::
[3]:2001:db8:0:1:1::
SA:2001::1
DA:2001:db8:0:3:48::
NH:RH
Type:4(SRH)
NH:IPv4|SL:1
Segment List:
[0]:2001:db8:0:4:eeee::
[1]:2001:db8:0:3:48::
[2]:2001:db8:0:2:1::
[3]:2001:db8:0:1:1::
SA:2001::1
DA:2001:db8:0:4:eeee::
NH:IPv4
Notes: Parent node: node where the segment was instantiated, and where it will be processed
Function could be the basic end-point behavior that I showed in the previous slides, or something much more sophisticated... even using arguments
Fliexible bit-length...
the only thing that matters to the rest of the network is that the parent node advertises the locator prefix, so that packets can be routed to it. What it then does with the packet, so the function, is purely local
Local address: address within the locator prefix, or assigned to an interface
conversely....

## Slide 19: SID Structure
1111:2222:3333:4444:5555:6666:7777:8888
128 Bits Like IPv6 address but different semantics
Locator
Function
Padding
Block
Node ID
Function
Argument
Padding

## Slide 20
SRv6 uSID

## Slide 21
SRv6 uSID format
2001 :0db8 : 0100 : 0200 : 0300 : 0400 : 0500 : 0000
SRv6 uSID
Block
SA:2001::1
DA:2001:db8:0:4:1:0:0:0
NH:RH
Type:4(SRH)
NH:IPv4|SL:1
Segment List:
[0]: 2001:db8:0:5:45:0:0:0
[1]: 2001:db8:0:4:1:0:0:0
[2]: 2001:db8:0:3:48:0:0:0
[3]: 2001:db8:0:2:1:0:0:0
[4]: 2001:db8:0:1:42:0:0:0
uSID
1
uSID
2
uSID
3
uSID
4
uSID
5
EoC
6
: 0100 :
=SRV6 uSID
SRV6 uSID Container
SRV6 Encapsulation
SRV6 uSID Encapsulation
SA:7.5.4.3
DA:11.6.19.71
Port:UDP
UDP Header/Data
SA:7.5.4.3
DA:11.6.19.71
Port:UDP
UDP Header/Data
SA:2001::1
DA:2001:db8:100:200:300:400:500::
NH:IPv4
16 bits here, but can be anything
32 bits here,
but can be anything
Notes: Parent node: node where the segment was instantiated, and where it will be processed
Function could be the basic end-point behavior that I showed in the previous slides, or something much more sophisticated... even using arguments
Fliexible bit-length...
the only thing that matters to the rest of the network is that the parent node advertises the locator prefix, so that packets can be routed to it. What it then does with the packet, so the function, is purely local
Local address: address within the locator prefix, or assigned to an interface
conversely....

## Slide 22
SRv6 uSID Possible Formats
fcbb :0102 : 0304 : 0506 : 0708 : 0901 : 0b0c : 0d0e
SRv6 uSID Block
uSID1
FXXYY. XX= Block size; Y=uSID size
uSID2
uSID3
uSID14
F1608
F4816
2001 :0db8 : aaaa : 0001 : 0002 : 0003 : 0004 : 0005
F3224
fcbb :bb00 : 0000 : 0100 : 0002 : 0000 : 0300 : 0004
Anything is possible
Notes: Parent node: node where the segment was instantiated, and where it will be processed
Function could be the basic end-point behavior that I showed in the previous slides, or something much more sophisticated... even using arguments
Fliexible bit-length...
the only thing that matters to the rest of the network is that the parent node advertises the locator prefix, so that packets can be routed to it. What it then does with the packet, so the function, is purely local
Local address: address within the locator prefix, or assigned to an interface
conversely....

## Slide 23
SRv6 uSID F3216
S
R1
R2
R3
R4
R
2001:db8:1::/48
2001:db8:2::/48
2001:db8:3::/48
2001:db8:4::/48
SA:2001::1
DA:2001:db8:1:2:3:e000:4:eeee
NH:IPV4
BGP:2001:db8:4:eeee::
SA:2001::1
DA:2001:db8:2:3:e000:4:eeee::
NH:IPV4
SA:2001::1
DA:2001:db8:3:e000:4:eeee::
NH:IPV4
SA:2001::1
DA:2001:db8:4:eeee::
NH:IPV4
Notes: Parent node: node where the segment was instantiated, and where it will be processed
Function could be the basic end-point behavior that I showed in the previous slides, or something much more sophisticated... even using arguments
Fliexible bit-length...
the only thing that matters to the rest of the network is that the parent node advertises the locator prefix, so that packets can be routed to it. What it then does with the packet, so the function, is purely local
Local address: address within the locator prefix, or assigned to an interface
conversely....

## Slide 24
SRv6 uSID More Than 6 SIDs?
2001 : 0db8 : 0100 : 0200 : 0300 : 0400 : 0500 : 0600
Container 1
SA:7.5.4.3
DA:11.6.19.71
Port:UDP
UDP Header/Data
SA:2001::1
NH:
100->200->300->400->500->600->700->800->900->a00->b00
2001 : 0db8 : 0700 : 0800 : 0900 : 0a00 : 0b00 : 0000
Container 2
Type:4(SRH)
NH:IPv4|
Segment List:
[0]: 2001:db8:700:800:900:a00:b00::
DA:2001:db8:100:200:300:400:500:600
DA:2001:db8:200:300:400:500:600:0
DA:2001:db8:300:400:500:600:0::
DA:2001:db8:400:500:600:0::
DA:2001:db8:500:600:0::
DA:2001:db8:600:0::
DA:2001:db8:700:800:900:a00:b00::
DA:2001:db8:800:900:a00:b00::
DA:2001:db8:900:a00:b00::
DA:2001:db8:a00:b00::
DA:2001:db8:b00::
Shift & Forward
END of Container
-> is there SRH?
Decrement SL
Copy New SID (Container)
PSP
SL:1
SL:0
1
2
3
4
6
7
9
b
5
a
8
RH
IPv4
Notes: Parent node: node where the segment was instantiated, and where it will be processed
Function could be the basic end-point behavior that I showed in the previous slides, or something much more sophisticated... even using arguments
Fliexible bit-length...
the only thing that matters to the rest of the network is that the parent node advertises the locator prefix, so that packets can be routed to it. What it then does with the packet, so the function, is purely local
Local address: address within the locator prefix, or assigned to an interface
conversely....

## Slide 25: Sets, Global ID Block (GIB), Local ID Block (LIB)
Within a Block, SIDs are allocated: FCBB:BB00:XXXX::/48
SID can be:
  Global: shortest path to a node – globally unique
  Local: a local function – not globally unique
GIB
LIB
0xffff
0xe000
0xdfff
0x0001

## Slide 26: Wide LIB
When more than 8k local IDs are needed, use Wide LIB
  WLIB provides 8 × 64k local IDs
WLIB is an extension to LIB
  A (special) ID in the LIB references another ID table (WLIB)​
    LIB IDs FFF0 to FFF7
  E.g., FCBB:BB00:FFF0:XXXX::/64 is a local uSID of WLIB
LIB and WLIB can concurrently be used on a node
LIB
GIB
0xE000
0xFFFF
8K
WLIB
0xFFF0
64K
0x0001
0xFFFF

## Slide 27: SRv6 uSID Configuration
segment-routing
srv6
locators
locator MAIN
micro-segment behavior unode psp-usd
prefix fcbb:bb00:1::/48
Name to reference
uSID
Locator Prefix

## Slide 28
destination address
hop limit
ver
tc
flow label
payload length
next header
source address
IPv6 Header
source IP address
ver
length
hl
tos
id
flags
fragment offset
ttl
protocol
header checksum
destination IP address
Flow Label
What for?
Entropy encoding encap
  5 Tuple Hash into flow label
Used for Hash on P routers
IP Header
4
TCP data
source port
destination port
sequence number
acknowledgment number
hlen
reserved
code bits
window
checksum
urgent
options
TCP Header
HASH

## Slide 29
PE1
P3
Flow Label
SA:1.1.1.1
DA:2.2.2.2
Prot:TCP
TCP sPort; dPort
SA:2001::1
DA:fcbb:bb00:3:e002::
NH:IPv4. FL:0x7543
SA:3.3.3.3
DA:4.4.4.4
Prot:TCP
TCP sPort; dPort
SA:1.1.1.1
DA:2.2.2.2
Prot:TCP
TCP sPort; dPort
SA:3.3.3.3
DA:4.4.4.4
Prot:TCP
TCP sPort; dPort
SA:2001::1
DA:fcbb:bb00:3:e002::
NH:IPv4. FL:0x1106
P2
P4
PE5
ECMP
FL used for hash
Notes: Simple move of LNX to node 4, change of some physical configas +some slides, visually not very nice…

## Slide 30
SRv6
Network Programming

## Slide 31
END– Default endpoint (Node SID)
Decrement SL
Copy Active SID
Forward
R1
SA:2001::1
DA:2001:db8:0:1:1::
NH:RH
Type:4(SRH)
NH:IPv4|SL:3
Segment List:
[0]:2001:db8:0:4:eeee::
[1]:2001:db8:0:3:e000::
[2]:2001:db8:0:2:1::
[3]:2001:db8:0:1:1::
SA:2001::1
DA:2001:db8:0:2:1::
NH:RH
Type:4(SRH)
NH:IPv4|SL:2
Segment List:
[0]:2001:db8:0:4:eeee::
[1]:2001:db8:0:3:e000::
[2]:2001:db8:0:2:1::
[3]:2001:db8:0:1:1::
R2
Different Flavors:
  End
  End with PSP
  End with USP
  End with PSP & USP
  End with USD
  End with PSP & USD
  End with USP & USD
  End with PSP, USP & USD
  End with NEXT-ONLY-CSID
  End with NEXT-CSID
  End with NEXT-CSID & PSP
  End with NEXT-CSID & USP
  End with NEXT-CSID, PSP & USP
  End with NEXT-CSID & USD
  End with NEXT-CSID, PSP & USD
  End with NEXT-CSID, USP & USD
  End with NEXT-CSID, PSP, USP & USD

## Slide 32
uN=END with Next – Default endpoint (Node SID)
Decrement SL
Copy Active SID
Forward
R1
SA:2001::1
DA:2001:db8:1:2:3:e000:4:eeee
NH:IPV4
SA:2001::1
DA:2001:db8:2:3:e000:4:eeee
NH:IPV4
R1
SA:2001::1
DA:2001:db8:0:1::
NH:RH
Type:4(SRH)
NH:IPv4|SL:3
Segment List:
[0]:2001:db8:4:eeee::
[1]:2001:db8:3:e000::
[2]:2001:db8:2::
[3]:2001:db8:1::
SA:2001::1
DA:2001:db8:2::
NH:RH
Type:4(SRH)
NH:IPv4|SL:2
Segment List:
[0]:2001:db8:4:eeee::
[1]:2001:db8:3:e000::
[2]:2001:db8:2::
[3]:2001:db8:1::
R2
R2
Shift & Forward
Better way:

## Slide 33
uA=END.X with Next – (Adjacency SID)
SA:2001::1
DA:2001:db8:3:e000:4:eeee::
NH:IPV4
SA:2001::1
DA:2001:db8:4:eeee::
NH:IPV4
Shift & Forward to SPECIFIC INTERFACE
R3
R4
Ten0/0/0/0
Ten0/0/0/1
uA 2001:db8:3:e000::
uA 2001:db8:3:e001::
R

## Slide 34
uDX4=END.DX4, uDX6=END.DX6, uDX2=END.DX2
Endpoint with Decapsulation and Xconnect
SA:2001::1
DA:2001:db8:4:eeee::
NH:IPV4
Decapsulate and Forward to SPECIFIC INTERFACE
Same as Per CE Label Allocation
Must be last function in SID list
R4
IPv4 Packet
IPv4 Packet
Ten0/0/0/0

## Slide 35
uDT4=END.DT4, uDT6=END.DT6
Endpoint with Decapsulation and Table Lookup
SA:2001::1
DA:2001:db8:4:eeee::
NH:IPV4
Decapsulate and Table Lookup (VRF)
Same as Per VRF Label Allocation (aggregate label)
Must be last function in SID list
R4
IPv4 Packet
IPv4 Packet

## Slide 36: SRv6 functions: Steering and Services
Codename |  | Behavior | 
End | uN | Endpoint | [Node SID]
End.X | uA | Endpoint with Layer-3 cross-connect | [Adj SID]
End.B6.Insert | uB6.Insert | Endpoint bound to an SRv6 policy | [BSID]
End.B6.Encap | uB6.Encaps | Endpoint bound to an SRv6 encapsulation policy | [BSID]
End.DX6 | uDX6 | Endpoint with decapsulation and IPv6 cross-connect | [L3VPN Per-CE]
End.DX4 | uDX4 | Endpoint with decapsulation and IPv4 cross-connect | [L3VPN Per-CE]
End.DT6 | uDT6 | Endpoint with decapsulation and specific IPv6 table lookup | [L3VPN Per-VRF]
End.DT4 | uDT4 | Endpoint with decapsulation and specific IPv4 table lookup | [L3VPN Per-VRF]
End.DX2 | uDX2 | Endpoint with decapsulation and L2 cross-connect | [E-LINE]
End.DT2U/M | uDT2U/M | Endpoint with decapsulation and L2 unicast lookup / flooding | [E-LAN]
End.DTM | uDTM | Endpoint with decapsulation and MPLS table lookup | [Interworking]
H.Insert / H.Encaps |  | Headend with Insertion / Encapsulation of / into an SRv6 policy | [TiLFA]
H. Encaps.L2 |  | H.Encaps Applied to Received L2 Frames | [L2 Port Mode]
H.Encaps.M |  | H.Encaps Applied to MPLS Label Stack | [Interworking]

## Slide 37
SRv6
ISIS Extensions

## Slide 38
Functions might be signaled differently
Signalling | IGP | BGP-LS | BGP-IP/VPN
End, uN | Yes | Yes | 
End.X, uA | Yes | Yes | 
End.T | Yes | Yes | 
End.DX4,uDX4 |  | Yes | Yes
End.DX6,uDX6 | Yes | Yes | Yes
End.DX2,uDX2 |  | Yes | Yes
END.DT4,uDT4 |  | Yes | Yes
End.DT6,uDT6 | Yes | Yes | Yes
End.B |  | Yes | 
Signalling | IGP | BGP-LS | BGP-IP/VPN
H.insert |  | Yes | 
H.Encap |  | Yes | 
Locator – routing table

## Slide 39
ISIS for SRv6
LSP (Link State Packet):
r2
TLVs:
Hostname: r2
Interfaces: Hu0/0/0/0
Hu0/0/0/1
Lo0
Hu0/0/0/0
Hu0/0/0/1
Neighbors: r1
r3
r1
r3
IP addresses: fcbb:0:2::1/128
2001:12::2/64
Lo0
fcbb:0:2::1/128
2001:12::2/64
Locator: fcbb:0:2::/48
Locator:
fcbb:0:2::/48
uN:fcbb:0:2::
Structure: BL=32;NL=16;FL=0,AL=80
uA:fcbb:0:2:e001::
uA:fcbb:0:2:e002::
uA:fcbb:0:2:e002::
uA:fcbb:0:2:e001::
Capabilities: Algorithms ……
SIDs can insert
SIDs can decap
……….
Structure: BL=32;NL=16;FL=16;AL=0
Structure: BL=32;NL=16;FL=16;AL=0
Structure: BL=32;NL=16;FL=0,AL=80
Structure: BL=32;NL=16;FL=16;AL=0
Structure: BL=32;NL=16;FL=16;AL=0
:
uN:fcbb:0:2::

## Slide 40
ISIS LSP Example
IS-IS 1 (Level-2) Link State Database
LSPID LSP Seq Num LSP Checksum LSP Holdtime/Rcvd ATT/P/OL
r2.00-00 0x00000009 0x4f06 1145 /1200 0/0/0
Area Address: 49
NLPID: 0x8e
Hostname: r1
IPv6 Address: 2001::2
Metric: 10 MT (IPv6 Unicast) IPv6 fcbb:bb00:2::1/128
Prefix Attribute Flags: X:0 R:0 N:1 E:0 A:0
Metric: 1 MT (IPv6 Unicast) IPv6 fcbb:bb00:2::/48
Prefix Attribute Flags: X:0 R:0 N:0 E:0 A:0
MT: IPv6 Unicast 0/0/0
SRv6 Locator: MT (IPv6 Unicast) fcbb:bb00:2::/48 D:0 Metric: 0 Algorithm: 0
Prefix Attribute Flags: X:0 R:0 N:0 E:0 A:0
END SID: fcbb:bb00:2:: uN (PSP/USD)
SID Structure:
Block Length: 32, Node-ID Length: 16, Func-Length: 0, Args-Length: 0
Router Cap: 0.0.0.0 D:0 S:0
IPv6 Router ID: 2001::2
SR Algorithm:
Algorithm: 0
Algorithm: 1
SRv6: O:0
Node Maximum SID Depth:
SRH Max SL: 3
SRH Max End Pop: 3
SRH Max T.insert: 3
SRH Max T.encaps: 4
SRH Max End D: 4
Metric: 10 MT (IPv6 Unicast) IS-Extended r1.00
Local Interface ID: 6, Remote Interface ID: 6
Interface IPv6 Address: 2001:12::2
Neighbor IPv6 Address: 2001:12::1
END.X SID: fcbb:bb00:2:e001:: B:0 S:0 P:0 uA (PSP/USD) Alg:0
SID Structure:
Block Length: 32, Node-ID Length: 16, Func-Length: 16, Args-Length: 0
Total Level-2 LSP count: 1 Local Level-2 LSP count: 0
Locator
Capabilities
END
END.X
SID Structure

## Slide 41
SRv6
BGP Overlay Services

## Slide 42
1
3
BGP
CE
CE
eBGP
10.1.21.21
10.1.21.1
2001::1
2001::3
10.3.22.3
10.3.22.22
eBGP
IPv4 :10.10.22.0/24
NH:10.3.22.22
VPNv4 :10.10.22.0/24
NH:2001::3
RD-1:1
RT -1:1
uDT4– fcbb:bb00:3:e002::
IPv4 :10.10.22.0/24
NH:10.1.21.1
uDT4 – fcbb:bb00:3:e002::
IPv6
No Changes Required!
Locator – fcbb:bb00:3::/48
iBGP
Notes: Simple move of LNX to node 4, change of some physical configas +some slides, visually not very nice…

## Slide 43
1
3
L3 VPN Dataplane
CE
CE
10.1.21.21
10.1.21.1
2001::1
2001::3
10.3.22.3
10.3.22.22
uDT 4– fcbb:bb00:3:e002::
IPv6
SA:10.10.21.10
DA:10.10.22.10
NH:UDP
UDP Header/Data
SA:10.10.21.10
DA:10.10.22.10
NH:UDP
UDP Header/Data
SA:2001::1
DA:fcbb:bb00:3:e002::
NH:IPv4
SA:10.10.21.10
DA:10.10.22.10
NH:UDP
UDP Header/Data
Notes: Simple move of LNX to node 4, change of some physical configas +some slides, visually not very nice…

## Slide 44
1
3
EVPN
CE
CE
2001::1
2001::3
EVPN :EVI 7543
NH:2001::3
RD-1:1
RT -1:1
uDX2– fcbb:bb00:3:e002::
uDX2 – fcbb:bb00:3:e002::
IPv6
No Changes Required!
Locator – fcbb:bb00:3::/48
EVI 7543
EVI 7543
iBGP
Notes: Simple move of LNX to node 4, change of some physical configas +some slides, visually not very nice…

## Slide 45
1
3
EVPN Dataplane
CE
CE
uDX2 – fcbb:bb00:3:e002::
IPv6
Locator – fcbb:bb00:3::/48
EVI 7543
EVI 7543
L2 Frame
SA:2001::1
DA:fcbb:bb00:3:e002::
NH:L2
L2 Frame
L2 Frame
Notes: Simple move of LNX to node 4, change of some physical configas +some slides, visually not very nice…

## Slide 46
SRv6 uSID
Conclusion

## Slide 47: SRv6 is Fully Standardized
Strong Cisco Commitment and Leadership
Editor of 96% IETF RFCs
Co-author of 100% IETF RFCs
SRv6 BGP Services – RFC 9252
SRv6 ISIS – RFC 9352
SR Flex-Algo – RFC 9350
Control Plane
SR Architecture – RFC 8402
SRTE Policy Architecture – RFC 9256
Compressed SRv6 Segment List – WG Draft
Architecture
SRv6 OAM – RFC 9259
Performance Management – RFC 5357
Operation &
Management
SRv6 Network Programming – RFC 8986
IPv6 SR header – RFC 8754
Data Plane

## Slide 48: Rich SRv6 uSID Ecosystem
Merchant Silicon
Smart NIC
Partners
Open-Source Applications
Network Equipment Manufacturers
Open-Source Networking Stacks
Pyroute2
SERA
BGP
FRRouting

## Slide 49: SRv6 … at Record-Speed
Deployed
Active Testing
Deployment Planned
Americas
EMEA
APJC
Chart: 
| Production | Lab | Early
SRv6 | 5 | 85 | 52
142
Chart: 
| Production | Lab | Early
SRv6 | 5 | 103 | 52
160
Chart: 
| Production | Lab | Early
SRv6 | 8 | 71 | 17
96
Notes: As of Sep 2023:
Total: 398
  18 Deployed
  380 Planned
21ViaNet ; 2Connect ; Acxiom ; AEW Energie ; Airtel - Bharti Airtel ; AIS ; Alibaba ; Altibox ; Altice - Dominicana (Tricom) ; Altice - France (SFR) ; Altitude Infrastructure ; AM Wireless ; America Movil - Brazil (Embratel) ; America Movil - Mexico (Telmex) ; Aricent ; Armasuisse ; Arvig Communication Systems ; Asset Black ; AT&T ; AT&T Entertainment (DirecTV) ; AT&T India ; Atlantic Broadband ; Aureon ; Aussie Broadband ; Axiata - Indonesia (XL) ; Axiata - Malaysia (Celcom) ; Axiata - Sri Lanka (Dialog) ; Axtel ; Bank of America (BofA) ; Bank of Canada ; Barry Communications ; Beanfield Metroconnect ; Bell Canada ; Belwue ; BMIT ; Bouygues (Bytel) ; British Telecom (BT) ; Cabo Telecom ; Camworth ; Carolina Connect ; CAT Telecom ; Cedar Falls Utilities ; Celeste ; CESNET ; Charter ; China Mobile ; China Network Systems ; China Next Generation Internet (CERNET2) ; China Telecom ; China Unicom ; China Zheshang Bank (CZBank) ; Chinabank ; CHT - Chunghwa Telecom ; City of Buenos Aires ; Claranet ; Cogeco - Peer1 ; Cogeco Cable ; Cogent ; COLT ; Com4 AS ; Comcast ; Comnets Plus ; Consolidated Communications ; COX Communications ; CRIANN ; Crnogorski Telekom ; Ctrip Computer Technology ; Cyberlink ; CyrusOne ; Deutsche Telekom ; Discover Financial ; Dish Network ; Dutch Department of Defense ; Earthlink ; Eastern Telecom - Philippines ; EchoStar (Hughes) ; Edward Jones Investments ; Eir Communications ; Elbit Systems ; Elisa ; Entel ; EOLO ; Etisalat - Saudi Arabia (Mobily) ; Etisalat - UAE ; European Commission ; European Union ; EWW Gruppe ; Facebook ; Fibia ; Flextential ; FREE ; G.Network ; General Datatech (GDT) ; Gila River Communications ; Google ; Google - India ; Google - Marconi ; Government of Switzerland ; Guadalupe Valley Communications ; Hans Networks ; HKT - Hong Kong Telecom ; iBasis ; Iliad - Italy ; Iliad - Jaguar Networks ; InfoWest ; Inteliquent ; Intelsat ; Internet Initiative ; Internet Solutions ; Internet2 ; Itochu Techno-Solutions ; Jack Henry & Associates ; James Valley Telecommunications ; JPMorgan Chase ; JT Group ; Jupiter Telecommunications ; KazTransCom ; KDDI ; Kentik ; KT - Korea Telecom ; Liberty Global ; Lightstorm Telecom ; LINE ; Link Net ; Link3 Technologies ; Lumen (CenturyLink) ; Maha IT ; Maintel ; Maroc Telecom ; MediaCom ; MegaFon ; Megaport ; MetroNet (Metro Fibernet) ; Metrotel ; Microsoft ; Microsoft Azure Cloud ; Morgan Stanley ; MTel Tecnologia ; MTN - Nigeria ; MTN - South Africa ; MTN - Uganda ; NATO ; Naver ; NBB Bank (National Bank of Belgium) ; NBN ; NEC ; Net Brazil ; Net One ; NetEase Games ; Netfast ; Network Solutions Group ; NJEdge ; Nordvest Fiber ; NOS Comunicacoes ; Nsight ; NSS S.A. ; NTT America ; NTT Communications ; NTT Docomo ; NTT East ; NTT France (SASU) ; NTT Germany ; NTT Netherlands ; NTT Poland (ZOO) ; NYU Medical Center ; Obos Opennet ; Oi (Telemar) ; OKI Electric ; Ooredoo - Indosat ; OpenNet Norge ; Optage ; Orange - Spain ; Oriental Cable Network ; OSHEAN ; Otecel ; Over The Wire ; OVHCloud ; Pacnet Business Solutions ; PCCW ; PenTeleData ; People's Bank of China ; Ping An Insurance ; PLDT ; Proximus ; Qatar Petrolium ; Qtel ; Rakuten ; Reliance Jio ; RENCI ; Rogers Communications ; RUAG ; RWS Group ; SALT ; SAP ; SAP - America ; SAP - Saudi Arabia ; Scanplus GmbH ; Schwarz ; Serpro ; Shanghai Broadband Company ; Shanghai Mobile Communications ; Shanxi Telecom ; Shaw Communications ; Sinsidocom ; SK Broadband ; SK Telecom ; SKY - Arabia ; SKY - Italia ; SKY - UK ; Smals ; Smartfren Telecom ; SoftBank ; Sony Corporation ; SRG SSR ; StarHub ; STC - Saudi Telecom Company ; Summit Communications ; Sweden Department of Defense ; Swisscom ; Switch GmbH ; Switzerland Department of Defense ; Symphony & Earthlink ; Tata Communications ; Telco OI ; Tele2 ; Telecom Argentina ; Telecom Egypt ; Telefonica – Brazil(Vivo); Telefonica - Czech Republic (O2) ; Telefonica - UK (O2) ; Telemach ; Telia ; Telia Finland ; Telia Lietuva (Omnitel) ; Telia Norge ; Telkomcel ; Telstra ; Telstra - CEVA ; Teracom Training Institute ; Terago ; TIM - Brazil ; T-Mobile - Austria ; T-Mobile - Hungary ; T-Mobile - Netherlands ; T-Mobile - Poland ; T-Mobile - USA ; T-Mobile (Sprint) ; TPG Telecom (VHA) ; TraxComm ; Trecom ; T-Systems - Austria ; T-Systems - Hungary ; Turkcell ; Twitch ; Twitter ; uCloud ; UEN (Utah Education Network) ; Ulta ; Unisys ; UPC Austria ; UPC Netherland ; US Air Force ; US Marshalls Service ; US Postal Service ; Verizon ; Verizon - India ; Verizon Business ; Verizon Wireless ; Viasat ; Videotron ; Viettel ; Vision Net ; Vodacom ; Vodafone - Germany ; Vodafone - Group ; Vodafone - Idea (Aditya) ; Wasu Media ; Wave Broadband ; Wells Fargo - Wachovia ; WIA ; World Wide Technology (WWT) ; Wuhan Cable ; Yandex ; YouFibre ; Zain - Kuwait ;

## Slide 50
Simplicity Always Prevails
Furthermore, with more scale
and functionality
LDP RSVP-TE
BGP 3108 MPLS UDP/VxLAN NSH

## Slide 51
Notes: Thank you very much, for watching this SRv6 usid introduction in 7.3.1 and I am already looking forward to show you some traffic engineering and layer 2 vpns which will be introduced in 7.3.2.
Good bye