## Slide 1: Prelude to a BGP hijack?
Improper uses of AS-sets?
Lasse Jarlskov
Lasse.jarlskov@teliacompany.com

## Slide 2: What happened?
Our upstream IP-transit provider alerted us.
An AS-SET in the RIPE DB suddenly showed up referencing our AS-number

## Slide 3: Who dis?
Clearly presenting the AS-set to their upstream:
Russia or Tehran, IR?

## Slide 4: What is an AS-SET anyway?
Just a list of AS’s
Can be used for anything:
  AS’s present at my IXP.
  AS’s I have a BGP-session with somewhere.
  AS’s whose sales-people bought me a beer at the latest conference.
Most common recommended usage:
  IP-transit providers filtering BGP-announcements from their customers
Example from MANRS:

## Slide 5: IP Transit filtering
ROA – Route Origin Authorisation
  Only validates the originating ASN
  Easily spoofed
RPSL-based filtering
  Based on AS-Set, route(6) and aut-num objects
  Best practice (MANRS)
Tier 1 upstream provider
Another Tier 1
Telia SE
AS3301
Attacker AS
Spoofed AS3301
RPSL-based filtering
Equal AS-path length
ROA VALID
Spoofed BGP announcement

## Slide 6: What can we do about fraudulent AS-sets?
ASPA
  Autonomous System Provider Authorization
  Currently going through IETF
  Not ready yet
Monitoring IRR’s
  IRRexplorer
  BGP.tools
  Etc.

## Slide 7: What to do? ASPA
ASPA was designed specifically against this
  Autonomous System Provider Authorization (ASPA)
  In short: “Who are my allowed upstreams?”
  https://datatracker.ietf.org/doc/draft-ietf-sidrops-aspa-verification/
  https://datatracker.ietf.org/doc/draft-ietf-sidrops-aspa-profile/
  Still being worked on in IETF – “Real Soon Now[tm]”
While waiting
  Monitor who are referencing you in IRR DBs.
Tier 1 upstream provider
Another Tier 1
Telia SE
AS3301
Attacker AS
Spoofed AS3301
RPSL-based filtering
Equal AS-path length
ASPA INVALID
ROA VALID
Spoofed BGP announcement

## Slide 8: What to do – right now? Monitoring IRRs
Search for your ASN / AS-Set
  E.g. bgp.tools, ”Whois” tab
  irrexplorer.nlnog.net
  Follow the chain of references
Some automated monitoring tools, can provide automated alerts for long reference chains

## Slide 9: Recursive monitoring
Many many many AS-sets with questionable semantic meaning
E.g. Telia does not peer at DECIX Düsseldorf

## Slide 10: What can we do about fraudulent AS-sets?
ASPA
  Autonomous System Provider Authorization
  Currently going through IETF
  Not ready yet
Monitoring IRR’s
  Why would you need a “Peering” AS-set?
  Are you sure your “Peering” AS-set actually only contains your peers?

## Slide 11: What are the ASPA components?
draft-ietf-sidrops-aspa-profile (how to encode ASPA objects in DER)
draft-ietf-sidorps-aspa-verification (how to apply ASPA to BGP)
draft-ietf-sidrops-aspa-slurm (defining local overrides)
draft-ietf-sidrops-8210bis (RPKI-To-Router specification)

## Slide 12: Soon: IETF SIDROPS WGLC
WGLC = Working Group Last Call (“speak now or silent forever”)
Operators must be able to test the system end-to-end
  Publish ASPA in test environment of RIR
  Run a validator to fetch it
  Feed it via RTR to a router
  See on the router which routes are rejected/accepted
  Use SLURM to locally override above results
The ASPA drafts are interconnected, they form a ‘cluster’

## Slide 13: Already today lots of software!
OpenBGPD
BIRD
Rpki-client
Routinator
Rtrlib
StayRTR
Next year: Cisco? Juniper? Huawei?
ASK YOUR VENDOR!