## Slide 1: SR BGP and Egress Peer Engineering (EPE)
Joachim Jerberg Jensen, CCIE-SP #42403
Solutions Architect – joajense@cisco.com
March 2025

## Slide 2: Peering Trends - New paradigm, new requirements
Traffic moving closer to users (MEC, CDN)
+80% of Traffic is video
Subscriber BW growing at 31% CAGR
Stricter peering SLAs with move to SaaS
Increased Peering Distribution

## Slide 3: Optimization and SLAs drive Peering Engineering
Best network exit path that is both cost-efficient and provides good user experience metrics (cost, link utilization & traffic loss, SLA’s/latency, disjointness etc.)
Optimal path across SP network for ingress traffic from peering location to SP end users
Optimal exit link chosen:
  SLA’s (Latency, disjointness etc.)
  Cost
SP WAN
Optimal exit link chosen:
  Low cost (private peer)
  Low utilization link
  SLA’s
  Egress
  Ingress
Todays topic

## Slide 4: BGP Path Selection Criteria
BGP route selections can be tricky to manipulate (Cold/Hot potato)
What if you want different egress routing behaviour depending on:
What PE you are at, and what specific prefix you target?
Latency?
Load on the links?
Co$t of the links and peerings? (Local, IXP, Transit)
Disjointness for specific customer SLA’s?
Or obtain:
Maximum load sharing (unequal?) of your egress traffic?
Better control of traffic to BGP peered CDNs? (Netflix, Google Caches)
Notes: Cold potato routing – send traffic to the most optimal exit – usually achieved by tuning BGP Local Preference
Hot potato routing – send traffic to the nearest exit – usually achieved by setting the same Local Preference and ignoring AS Path for BGP best path, so that the exit is picked by lowest IGP metric

## Slide 5: Egress Peer Engineering (Centralized)
Egress Peer Engineering problem statement: “A centralized controller should be able to instruct an ingress PE or a content source within the domain to use a specific egress PE and a specific external interface/neighbor to reach a particular destination.” draft-filsfils-spring-segment-routing-central-epe
Conceptually Introduced by Cisco at NANOG6, first draft from May 2014.
Become RFC 9087 in Aug 2021 - Segment Routing Centralized BGP Egress Peer Engineering
Leverage defined concepts of RFC8402 (Segment Routing Architecture), BGP Peering Segments

## Slide 6: Egress Peer Engineering (Centralized)
Egress Peer Engineering (EPE) require no change in the existing BGP network design
EPE functionality is only required border router and EPE controller (SR-PCE)
The SR-PCE collects topology information (w. BGP-LS), including the EPE information, and uses that information to compute and implement *per-flow* traffic steering
Per-flow Policy state is only created on the ingress node
Segment Routing based
This may theoretically be *any* XR router Virtual recommended for production. Manual configuration is also an option

## Slide 7: Segment Routing Basic Operation and Segment Types
65
A packet injected anywhere with top label 65 will reach Z
Nodal/Prefix Segment: label allocated from the SR registry to each node. Globally significant. For example Z is given label 65.
9001
Adjacency Segment: Node automatically allocates a local label for each adjacency. Locally significant. For example Label 9001 allocated for adjacency O.
A packet injected at node C with label 9001 is forced through datalink CO
A
B
C
M
N
O
Z
D
P
A
B
C
D
Z
M
N
O
P
Source Routing: The source chooses a path and encodes it in the packet header as an ordered list of segments.
Segment: An identifier for any type of instruction i.e. "go to node C using the shortest path"

## Slide 8: Segment Routing Label Usage
Any explicit path can be expressed i.e. ABCOPZ
A
B
C
M
N
O
Z
D
P
9001
Packet to Z
65
9001
Packet to Z
65
Packet to Z
Packet to Z
65
Packet to Z
65
9001
72
Packet to Z
65
9001
72
72
72
65
65
A
B
C
D
Z
M
N
O
P

## Slide 9: BGP SR Peering Segments [RFC 8402]
AS 200
PeerAdj SID 15200
PeerAdj SID 15201
PeerNode SID 15300
PeerSet SID 15400
AS 500
Allows overriding default forwarding behavior to EBGP peers by using a specific local SID as the last SID in the SR SID list
PeerNode SID “go to this peer” - allows balancing traffic out multiple interfaces to the same peer
PeerAdj SID “go to this link” - allows sending traffic out specific peer interfaces
PeerSet SID. “go over a set of peers/links” Allows sending traffic out multiple interfaces to peers on the same or different nodes
SID’s can be configured locally on the ASBR’s for persistent values
AS 100
AS 600
ASBR

## Slide 10: Example Reference Topology
AS1 has an ingress Node1 and two egress Node2 and Node3
AS6 advertises a BGP prefix 6.1.1.0/24 to AS4 and AS5
AS1 peers with AS4 (Node4) and AS5 (Node5)
Node1’s BGP best path to BGP destination 6.1.1.0/24 in AS6 is via egress Node2 and Node4 (AS4)

## Slide 11: Egress Peer Engineering – Yes.. SR is enabled…
4
AS1
AS4
AS5
AS6
6
10
11
5
Segment
Routing
1
Payload
16003
3
2
router isis 1
interface Loopback0
address-family ipv4 unicast
prefix-sid absolute 16003
RP/0/0/CPU0:xrvr-1#traceroute 1.1.1.3
Type escape sequence to abort.
Tracing the route to 1.1.1.3
1 99.1.10.10 [MPLS: Label 16003 Exp 0] 9 msec 9 msec 9 msec
2 99.10.11.11 [MPLS: Label 16003 Exp 0] 19 msec 9 msec 19 msec
3 99.3.11.3 9 msec 9 msec 9 msec
Traceroute from 1 to 3

## Slide 12: EPE configuration example
10
11
4
AS1
AS4
AS5
AS6
6
5
eBGP
eBGP
Single-hop eBGP
Multi-hop eBGP
1
3
router bgp 1
bgp router-id 1.1.1.2
address-family ipv4 unicast
!
neighbor 1.1.1.5
remote-as 5
ignore-connected-check
egress-engineering
description eBGP peer xrvr-5
update-source Loopback0
address-family ipv4 unicast
route-policy bgp_in in
route-policy bgp_out out
!
neighbor 99.2.4.4
remote-as 4
egress-engineering
description eBGP peer xrvr-4
address-family ipv4 unicast
route-policy bgp_in in
route-policy bgp_out out
!
!
!
Node5
loopback
Link to Node4
2

## Slide 13: Advertising BGP Peering SIDs in BGP-LS
BGP-LS carries internal topology information as well as external connectivity (EPE) information
Egress Peer Engineering enabled egress nodes automatically advertise their BGP Peering SIDs in BGP-LS
  Each EPE egress node must have a BGP-LS session directly to the Controller or via a RR
Controller can use the BGP-LS information to compute and implement per-flow traffic steering
AS1
AS4
AS5
AS6
6
4
3
2
5
SR-PCE
EPE Controller
BGP-LS
Note: An IOS XR router is acting as “Controller” for illustration purposes
RP/0/0/CPU0:xrvr-10#show bgp link-state link-state [E][B][I0x0][N[c1][b0.0.0.0][q1.1.1.2]][R[c5][b0.0.0.0][q1.1.1.5]][L[i1.1.1.2][n1.1.1.5]]/664 detail
BGP routing table entry for [E][B][I0x0][N[c1][b0.0.0.0][q1.1.1.2]][R[c5][b0.0.0.0][q1.1.1.5]][L[i1.1.1.2][n1.1.1.5]]/664
NLRI Type: Link
Protocol: BGP
Identifier: 0x0
Local Node Descriptor:
AS Number: 1
BGP Identifier: 0.0.0.0
BGP Router Identifier: 1.1.1.2
Remote Node Descriptor:
AS Number: 5
BGP Identifier: 0.0.0.0
BGP Router Identifier: 1.1.1.5
Link Descriptor:
Local Interface Address IPv4: 1.1.1.2
Neighbor Interface Address IPv4: 1.1.1.5
Versions:
Process bRIB/RIB SendTblVer
Speaker 5 5
Flags: 0x04000001+0x00000000;
Last Modified: Oct 6 20:14:51.140 for 1d00h
<continue...>
“Protocol ID” field
“Identifier” field
“AS Number” TLV
“BGP-LS ID” TLV
“BGP Router-ID” TLV
“AS Number” TLV
“BGP-LS ID” TLV
“BGP Router-ID” TLV
BGP session local address
BGP session peer address
Peer Node SID 30035

## Slide 14
Controller and BGP LU – Could be PCEP, NETCONF Use low-latency path for Mr. Important NET Eng.
Controller sends a more preferred BGP-LU update to ingress node 1
NLRI: the destination prefix to Mr. Important NET Engineer, 6.1.1.6/32
Nhop: the selected egress border router. Which is node 3, and via link to R5
Label: the selected egress peer node SID—30035
AS path: reflecting the valid AS path selected to reach the destination

## Slide 15
Configuring the EPE Controller
Route policy is being used to define the next hop, local preference and label value for the given destination
This information is advertised to node 1 with the use of BGP-LU

## Slide 16
Egress Peer Engineering with controller
Ingress node 1 pushes the label stack on packets to 6.1.1.6/32
{prefix-SID(egress Node3); peerNode-SID(AS5 peer 5)}={16003; 30035}
Traffic steering on node 1 is per BGP destination
Example: for traffic destined to 6.1.1.6/32, impose {16003; 30035}

## Slide 17: Got it? Other EPE Use Cases

## Slide 18: Use case: Combine EPE with additional SR-TE
NCS 5501
NCS 5502
NCS Pyke J+
NCS 5504
NCS 5502
NCS Oldcastle J+
Problem: Engineering the best network exit path that is cost-efficient while providing special user experience metrics (latency, link utilization, disjoint & traffic loss).
Optimal exit link chosen:
  Low cost (private peer)
  Low utilization link
Advertising:
10.0.0.0/24
SP Network
Transit
Advertising:
10.0.0.0/24
Private Peer
92%
load

## Slide 19: Use case: PeerSet for maximum load balance
NCS 5501
NCS 5502
NCS Pyke J+
NCS 5504
NCS 5502
NCS Oldcastle J+
16001
16005
AS 1001
Loopback1 172.16.1.1
SID: 17001
SID: 17001
SID: 16001
SID: 15001
DSTIP: 10.0.0.1
DSTIP: 10.0.0.1
Push {17001,16001,15001}
Pop {17001}
Pop {16001}
AS 1002
PeerSet SID: 15001
SID: 15001
DSTIP: 10.0.0.1
Pop {15001} and forward
16004
AS 1003
Ingress
Traffic
Balance traffic to three peers even if normal BGP best path selection and forwarding would only select a single peer. Per-Flow load balancing is based on hashing criteria, SR retains ECMP across entire network
SID: 16001
SID: 15001
DSTIP: 10.0.0.1
Anycast SID
10.0.0.0/24
10.0.0.0/24
10.0.0.0/24

## Slide 20: Use case EPE and Weighted ECMP
3
4
6
5
1
SR PCE
2
Policy P(green, 1.1.1.5)
Binding-SID 4001
SID List <16005, 24001> Weight: 80%
SID List <16004, 24003> Weight: 20%
ISP A
Premium Content
ISP C
Premium Content
ISP B
EPE
24000
EPE
24003
Go to Node 5 (following IGP SPT) and exit via BGP peer adjacency 24001 to ISP A
Go to Node 4 (following IGP SPT) and exit via BGP peer adjacency 24003 to ISP C
EPE enabled on external peering links
EPE
24001
UCMP across SID lists using different weights
SR-MPLS
Local SR Policy configured at HE
*or*
SR PCE advertised SR Policy via PCEP / BGP
SR Policy (color, endpoint) @ HE X
e.g. (green, 1.1.1.5) @ Node (1)
IMPORTANT property:
The SR Policy endpoint (e.g. (5)) is decoupled from the target node specified in SID list (e.g. (4))

## Slide 21: SR Policy – Degradation Starts
3
4
6
5
1
SR PCE
2
Policy P(green, 1.1.1.5)
Binding-SID 4001
SID List <16005, 24001> Weight: 60%
SID List <16004, 24003> Weight: 40%
ISP A
Premium Content
ISP C
Premium Content
ISP B
Modified weights allow less traffic (from 80% to 60%) to be directed to ISP A and more traffic (from 20% to 40%) towards ISP C
Node (5) experiences partial failure of bundle to ISP A
X
External logic can be used to modify (re-configure) or re-advertise SR Policy
e.g.
adjusting weights of SID lists
EPE
24000
EPE
24003
EPE
24001
SR-MPLS
IMPORTANT property:
Only SR Policy is re-advertised
NO re-advertisement of end-user prefixes is required

## Slide 22
Use case: EPE for Cache Farm BW optimized peering
Y
Z
X
Cache
Cache Ctrl
MPLS
MPLS
YANG
Cache
MPLS
YANG
Cache
MPLS
MPLS
YANG
Cache
MPLS
YANG
RT1
RT2
B
A
172.0.1.1
172.0.2.1
WAN
172.1.X.X
RT3
RT4
loop0
200
101
102
103
loop0
202
loop0
202
loop0
204
a.a.a.0/24
IP dest a.a.a.x
101
200
IP dest a.a.a.x
101
To a.a.a.a/24
Use 101/200
Telemetry:
BW utilization
Responce time
Paket drop
50%
93%
90%
IP dest a.a.a.x
BGP
BGP Local-RIB
IGP topology
Node-SID
EPE-SID
Cache topo
Telemetry
Cache RIB’s
172.0.2.1
Cache RIB’s
172.0.1.1
API
External influence

## Slide 23: Use case: EPE for DDoS Traffic Steering
Transit 1
SP Network
Transit 2
Peer 1
DDoS Detection
Scrubbers
BGP Flowspec Rules
RR
EPE SID: 28000
EPE SID: 28001
SID: 16441
Egress Peer Engineering direct DDoS traffic to a specific end node and specific DDoS destination interface without the complexities of using VRFs to separate dirty/clean traffic.
no IP lookup is performed between the ingress node and egress DDoS “dirty” interface.
BGP Flowspec redirects traffic to a next-hop IP pointing to a pre-configured “DDoS” SR-Policy.