## Slide 1: Flowspec Peter Lundqvist peter@arista.com

## Slide 2: Flowspec

## Slide 3: Flowspec
Been around for some time…
  However limited attraction until recently…
Now the indication it’s a game changer DDoS/Mitigation industry
  Opens up alternatives both regards design and the selection of tools/vendors
Traffic can now be dropped directly at the BGP edge peering, based on information from mitigation device/controller basis of collected statistic
  But of course be just shaped alt relay the same way as with onramp&offramp
However Flowspec can do more…
Internet
Customer
/DC
Sflow/Telemetry
Flowspec Controller
Flowspec
BGP update
1.0.0.0/24
1.0.0.1/32
Core

## Slide 4: Flowspec signaled from customer to provider
This is unrealistic scenario !
This scenario comes up from time to time in Whitepapers written by vendors.
Never really been implemented in real solutions with scale and control
The problems (to begin with)
  Trust
  Scale&control
  Detection
  Etc…
Internet
Customer
Network/DC
Flowspec
BGP update
1.0.0.0/24
1.0.0.1/32
Operator
Core
PE (Provider)
CE/CPE (Customer)
Internet
>1.0.0.1/32
Notes: Trust
Do you really trust someone else to handle the mitigation by delegate the decision block your own (expensive) links ?
Operators most often not even trust customers routing updates without serious Adj-RIB-In filtering?
Scale&control
If propagate through the network, you have to adapt to the weakest chain of TCAM support on active platforms in your network regards scale of Flowspec rules
  Tools like max-prefix for rules have to be enable for Routers in the core to avoid TCAM explosion
Alt advanced COMMUNITIES design that decide where to deploy rules (then what is the purpose accept Flowspec from customer if no trust ?)
Detection
Where to detect ? Customer CE or Customer DC… ?
Alt Operator trigger detection based on Slow/Telemetry and inform customer, but again why then run Flowspec interaction with the customer?

## Slide 5: Flowspec manage by Operator and controller
This is a realistic scenario
Flowspec advertisement NOT blindly
Rules advertised that possible knock out all traffic to a specific host within a specific port range on certain peer/Link, not whole FIB (or network).
Instead propagated where Statistics (Sflow/Telemetry) indicate there are DDoS event
The Gain:
  Capacity
  Flowspec installed where needed
  Mix of actions
Internet
Customer
Network/DC
1.0.0.0/24
>1.0.0.1/32
(Good and Bad traffic)
Operator
Core
Internet
>1.0.0.1/32
(Good traffic)
Controller/Scrubber
Notes: Capacity
  The Nodes capacity regards TCAM and other hardware dependency easy controlled since Flowspec sessions/rules only where it make sense
Flowspec installed only where needed
  Flowspec specific to Peer/Node/Customer interfaces where traffic enters => Flowspec installed only where its needed
Mix of actions
  Drop, rate-limit, relay can be used based on demands
  Example stages of them (start with relay, follow by rate-limit and perhaps in the end just drop in case shape not enough

## Slide 6: Flowspec Theory

## Slide 7: Flowspec Theory
The main go-to-source regards Flowspec is RFC5575
  Then there are RFC and Drafts mostly related to actions
BGP Flowspec draft was submitted to IETF on August 14th, 2007, and it was later published in 2009 as RFC 5575http://tools.ietf.org/html/rfc5575).
BGP Flowspec is a DDoS mitigation solution, by installing Flow related ACLs based on N-tuple information.
The filter can be related to the attacker or the victim or both. The main idea is to walk away from punish whole prefix and thereby cause blackhole for “innocent” sessions, instead punish either individual flows or aggregation of flows.

## Slide 8: Flowspec, Multiprotocol extension to BGP
Flowspec yet another Multiprotocol extension to the BGP protocol (SAFI 133)
Like any other capability its negotiated under the BGP OPEN phase
Several capabilities more and less default enable when run Flowspec
  Multiprotocol extension
  Route-refresh
  4 Byte AS
  ADD-PATH
  Etc…
(…)
Border Gateway Protocol - OPEN Message
Marker: ffffffffffffffffffffffffffffffff
Length: 49
Type: OPEN Message (1)
Version: 4
My AS: 64515
Hold Time: 180
BGP Identifier: 192.168.0.68
Optional Parameters Length: 20
Optional Parameter: Capability
Parameter Type: Capability (2)
Parameter Length: 6
Type: Multiprotocol extensions capability (1)
Length: 4
AFI: IPv4 (1)
Reserved: 00
SAFI: Flow Spec Filter (133)
Optional Parameter: Capability
Parameter Type: Capability (2)
Parameter Length: 2
Capability: BGP-Extended Message
Type: BGP-Extended Message (6)
Length: 0
(…)

## Slide 9: Flowspec rules
Flowspec message are MP_REACH_NLRI
The Flowspec Rules > FLOW_SPEC_NLRI similar to a “normal IP” route
But Rules are ACL to be installed in the TCAM
Like any ACL, Rules can be simple or in a more detail design
  Here a basic IP src/dst drop rule
Actions are carried > EXT-COMMUNITIES
  Here action: rate 0 => drop all in Flowspec terms
(…)
Path Attribute - EXTENDED_COMMUNITIES
Flags: 0xc0, Optional, Transitive, Complete
Carried extended communities: (1 community)
Flow spec traffic-rate: ASN 0, 0.000 Mbps [Transitive]
Type: Transitive Experimental (0x80)
1... .... = IANA Authority: Allocated
.0.. .... = Transitive across AS: Transitive
Subtype (Experimental): Flowspec traffic-rate (0x06)
2-Octet AS:
Rate shaper: 0
(…)
Path Attribute - MP_REACH_NLRI
Flags: 0x80, Optional, Non-transitive, Complete
Type Code: MP_REACH_NLRI (14)
Length: 18
Address family identifier (AFI): IPv4 (1)
Subsequent address family identifier (SAFI): FlowSpec (133)
Next hop network address (0 bytes)
Number of Subnetwork points of attachment (SNPA): 0
Network layer reachability information (13 bytes)
FLOW_SPEC_NLRI (13 bytes)
NRLI length: 12
Filter type: Destination prefix filter (1)
10.10.10.1/32
Filter type: Source prefix filter (2)
11.11.11.1/32
(…)

## Slide 10: Flowspec types theory
Type 1-12 ====>
Excluded 13 “Flow label”

## Slide 11: Flowspec rules…
However with Flowspec, “Rules” can be as wide as you want since flags can be used
  Equal ( = )
  Greater than ( > )
  Less than ( < )
  Or Regular-expression combination
Example here matches ==>
  Destination prefix: 10.10.10.1/32
  Source prefix: 11.11.11.1/32
  Next protocol: TCP (6)
  Destination port: 80-65535
  Source port: 1025-65535
(…)
FLOW_SPEC_NLRI (23 bytes)
NRLI length: 22
Filter: Destination prefix filter (10.10.10.1/32)
Filter type: Destination prefix filter (1)
10.10.10.1/32
Filter: Source prefix filter (11.11.11.1/32)
Filter type: Source prefix filter (2)
11.11.11.1/32
Source IP filter prefix length: 32
Source IP filter: 11.11.11.1
Filter: Protocol / Next Header filter (=6)
Filter type: Protocol / Next Header filter (3)
Operator flags: 0x81, end-of-list, Value length: 1 byte: 1 <<,equal
1... .... = end-of-list: Set
.0.. .... = and: Not set
..00 .... = Value length: 1 byte: 1 << (0)
.... 0... = Reserved: Not set
.... .0.. = less than: Not set
.... ..0. = greater than: Not set
.... ...1 = equal: Set
Decimal value: 6
Filter: Destination port filter (>79)
Filter type: Destination port filter (5)
Operator flags: 0x82, end-of-list, Value length: 1 byte: 1 <<,greater than
1... .... = end-of-list: Set
.0.. .... = and: Not set
..00 .... = Value length: 1 byte: 1 << (0)
.... 0... = Reserved: Not set
.... .0.. = less than: Not set
.... ..1. = greater than: Set
.... ...0 = equal: Not set
Decimal value: 79
Filter: Source port filter (>1024)
Filter type: Source port filter (6)
Operator flags: 0x92, end-of-list, Value length: 2 bytes: 1 <<,greaterthan
1... .... = end-of-list: Set
.0.. .... = and: Not set
..01 .... = Value length: 2 bytes: 1 << (1)
.... 0... = Reserved: Not set
.... .0.. = less than: Not set
.... ..1. = greater than: Set
.... ...0 = equal: Not set
Decimal value: 1024

## Slide 12: Flowspec rules…
More verbose rule
Here Type 5 (Dst Port) rule section
Example here matches ==>
  Destination prefix: 10.10.10.1/32
  Source prefix: 11.11.11.1/32
  Next protocol: TCP (6)
  Destination port: 80,8080-8088
  Source port: 1024-65535
(…)
Filter: Destination port filter (=80 || >8080 && <8088)
Filter type: Destination port filter (5)
Operator flags: 0x01, Value length: 1 byte: 1 <<, equal
0... .... = end-of-list: Not set
.0.. .... = and: Not set
..00 .... = Value length: 1 byte: 1 << (0)
.... 0... = Reserved: Not set
.... .0.. = less than: Not set
.... ..0. = greater than: Not set
.... ...1 = equal: Set
Decimal value: 80
Operator flags: 0x12, Value length: 2 bytes: 1 <<, greater than
0... .... = end-of-list: Not set
.0.. .... = and: Not set
..01 .... = Value length: 2 bytes: 1 << (1)
.... 0... = Reserved: Not set
.... .0.. = less than: Not set
.... ..1. = greater than: Set
.... ...0 = equal: Not set
Decimal value: 8080
Operator flags: 0xd4, end-of-list,Value length: 2bytes: 1 <<less than
1... .... = end-of-list: Set
.1.. .... = and: Set
..01 .... = Value length: 2 bytes: 1 << (1)
.... 0... = Reserved: Not set
.... .1.. = less than: Set
.... ..0. = greater than: Not set
.... ...0 = equal: Not set
Decimal value: 8088
Filter: Source port filter (>=1024)
Filter type: Source port filter (6)
Operator flags: 0x93, end-of-list, Value length: 2bytes:1 <<greater than,equal
1... .... = end-of-list: Set
.0.. .... = and: Not set
..01 .... = Value length: 2 bytes: 1 << (1)
.... 0... = Reserved: Not set
.... .0.. = less than: Not set
.... ..1. = greater than: Set
.... ...1 = equal: Set
Decimal value: 1024

## Slide 13: Flowspec CLI example

## Slide 14: Flowspec Configuration
Flowspec rules installed only on interfaces with “flow-spec” keyword enable
BGP session needs SAFI 133 enable “address-family flow-spec”
!
interface Ethernet7
description to attacker trident1
load-interval 5
no switchport
flow-spec ipv4 ipv6
ip address 6.6.6.2/24
!
(…)
router bgp 1111
router-id 111.111.111.111
(…)
neighbor 64515 peer-group
neighbor 64515 remote-as 64515
neighbor 64515 route-map med in
neighbor 64515 send-community
neighbor 64515 maximum-routes 0
(…)
neighbor 192.168.0.67 peer-group 64515
neighbor 192.168.0.68 peer-group 64515
!
address-family flow-spec ipv4
neighbor 64515 activate
!
address-family ipv4
no neighbor flow activate
!
(…)

## Slide 15: Flowspec RIB/FIB
Follows the BGP semantics but demands “flow-spec” keyword
Flowspec have the BGP components
  Adj-RIB-In
  Loc-RIB
  FIB
qumran-flowspec#sh bgp neighbors 192.168.0.68 flow-spec ipv4 received-routes detail
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;IP:=6;DP:>=80;SP:>=1024;
Rule identifier: 3890448648
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
IP Protocol: =6
Destination Port: >=80
Source Port: >=1024
Paths: 1 available
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric -, localpref -, weight 0, valid, external, best
Actions: Drop
Loc-RIB
Adj-RIB-In
Adj-RIB-In
BGP 192.168.0.68 received
FIB
BGP 192.168.0.67 received

## Slide 16: Flowspec RIB/FIB…
Flowspec have the BGP components
  Adj-RIB-In
  Loc-RIB
  FIB
qumran-flowspec#sh bgp flow-spec ipv4 detail
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;IP:=6;DP:>=80;SP:>=1024;
Rule identifier: 3890448648
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
IP Protocol: =6
Destination Port: >=80
Source Port: >=1024
Paths: 1 available
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Drop
BGP Flow Specification Matching Rule for 120.120.120.1/32;121.121.121.1/32;
Rule identifier: 3890488512
Matching Rule:
Destination Prefix: 120.120.120.1/32
Source Prefix: 121.121.121.1/32
Paths: 1 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Drop
Loc-RIB

## Slide 17: Flowspec EOS RIB/FIB…
Flowspec have the BGP components
  Adj-RIB-In
  Loc-RIB
  FIB (TCAM or FSIB)
qumran-flowspec#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;IP:=6;DP:>=80;SP:>=1024;
Rule identifier: 3890448648
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Next protocol: 6
Destination port: 80-65535
Source port: 1024-65535
Actions:
Drop
Status:
Installed: yes
Counter: 0 packets
Flow-spec rule: 120.120.120.1/32;121.121.121.1/32;
Rule identifier: 3890488512
Matches:
Destination prefix: 120.120.120.1/32
Source prefix: 121.121.121.1/32
Actions:
Drop
Status:
Installed: yes
Counter: 0 packets
FIB

## Slide 18: Hardware TCAM counters
On interfaces where Flowspec rules will be installed, static ACL and Flowspec rules do work side by side in most vendors implementations
qumran-flowspec#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3882113096
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Actions:
Drop
Status:
Installed: yes
Counter: 31 packets
Notes: To have counters for flowspec and not ACL (resources)
    “hardware counter feature flow-spec in”
    “no hardware counter feature acl in”

## Slide 19: Hardware TCAM profile…
hardware tcam
profile flowspec
feature acl port ip
sequence 45
key size limit 160
key field dscp dst-ip ip-frag ip-protocol l4-dst-port l4-ops l4-src-port src-ip tcp-control ttl
action count drop
packet ipv4 forwarding bridged
packet ipv4 forwarding routed
packet ipv4 forwarding routed multicast
packet ipv4 mpls ipv4 forwarding mpls decap
packet ipv4 mpls ipv6 forwarding mpls decap
packet ipv4 non-vxlan forwarding routed decap
packet ipv4 vxlan eth ipv4 forwarding routed decap
packet ipv4 vxlan forwarding bridged decap
!
feature flow-spec port ipv4
key size limit 160
key field dscp dst-ip ip-frag ip-protocol l4-dst-port l4-ops l4-src-port src-ip tcp-control
action count redirect
packet ipv4 forwarding routed
!
feature flow-spec port ipv6
key field dst-ipv6 ipv6-next-header ipv6-traffic-class l4-dst-port l4-ops-3b l4-src-port src-ipv6 tcp-control
action count redirect
packet ipv6 forwarding routed
!
system profile flowspec
With example Jericho hardware… TCAM profile changes for Flowspec needed

## Slide 20: Flowspec actions

## Slide 21: Flowspec actions
There are some main actions
  Drop (rate-limit=0)
  Redirect IP nexthop
  Redirect VRF IP nexthop (VRF-Lite)
  Redirect IP nexthop GRE
  Redirect VRF labeled nexthop (L3VPN)
  Etc…
RFC5575 define additional actions (DSCP, Sampling etc…)
Little up to each implementation…
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
Actions: Drop

## Slide 22: Flowspec drop rule
Flowspec action EXTENDED_COMMUNITIES
The Flowspec Rules FLOW_SPEC_NLRI
Drop (rate-limit=0 Flowspec term) the most basic of all rules, in brief just drop ANY matching traffic for the installed rule
Example here matches ====>
  Destination prefix: 10.10.10.1/32
  Source prefix: 11.11.11.1/32
  Next protocol: ICMP (1)
(…)
Path Attribute - EXTENDED_COMMUNITIES
Flags: 0xc0, Optional, Transitive, Complete
Type Code: EXTENDED_COMMUNITIES (16)
Length: 8
Carried extended communities: (1 community)
Flow spec traffic-rate: ASN 0, 0.000 Mbps [Transitive Experimental]
Type: Transitive Experimental (0x80)
1... .... = IANA Authority: Allocated
.0.. .... = Transitive across AS: Transitive
Subtype (Experimental): Flow spec traffic-rate (0x06)
2-Octet AS: 0
Path Attribute - MP_REACH_NLRI
Flags: 0x80, Optional, Non-transitive, Complete
Type Code: MP_REACH_NLRI (14)
Length: 21
Address family identifier (AFI): IPv4 (1)
Subsequent address family identifier (SAFI): Flow Spec Filter (133)
Next hop network address (0 bytes)
Number of Subnetwork points of attachment (SNPA): 0
Network layer reachability information (16 bytes)
FLOW_SPEC_NLRI (16 bytes)
NRLI length: 15
Filter: Destination prefix filter (10.10.10.1/32)
Filter type: Destination prefix filter (1)
Destination IP filter prefix length: 32
Destination IP filter: 10.10.10.1
Filter: Source prefix filter (11.11.11.1/32)
Filter type: Source prefix filter (2)
Source IP filter prefix length: 32
Source IP filter: 11.11.11.1
Filter: Protocol / Next Header filter (=1)
Filter type: Protocol / Next Header filter (3)
Operator flags: 0x81, end-of-list, Value length: 1 byte: 1 <<, equal
1... .... = end-of-list: Set
.0.. .... = and: Not set
..00 .... = Value length: 1 byte: 1 << (0)
.... 0... = Reserved: Not set
.... .0.. = less than: Not set
.... ..0. = greater than: Not set
.... ...1 = equal: Set
Decimal value: 1
(…)

## Slide 23: Flowspec action Drop
Actions: Drop
qumran-flowspec(config)#sh bgp flow-spec ipv4 det
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;IP:=1;
Rule identifier: 3882112672
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
IP Protocol: =1
Paths: 1 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric -, localpref 100, weight 0, valid, external, best
Actions: Drop
qumran-flowspec(config)#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;IP:=1;
Rule identifier: 3882112672
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Next protocol: 1
Actions:
Drop
Status:
Installed: yes
Counter: 32 packets
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67

## Slide 24: Flowspec redirect to IP rule
Flowspec action EXTENDED_COMMUNITIES
Redirect to IP nexthop
  Two drafts exist, most vendors support both
  Redirect to Nexthop (type 0x08)
  https://tools.ietf.org/html/draft-simpson-idr-flowspec-redirect-02
    Redirect to IP (type 0x8108)
  https://tools.ietf.org/html/draft-ietf-idr-flowspec-redirect-ip-02
(…)
Path Attribute - EXTENDED_COMMUNITIES
Flags: 0xc0, Optional, Transitive, Complete
1... .... = Optional: Set
.1.. .... = Transitive: Set
..0. .... = Partial: Not set
...0 .... = Extended-Length: Not set
.... 0000 = Unused: 0x0
Type Code: EXTENDED_COMMUNITIES (16)
Length: 8
Carried extended communities: (1 community)
Unknown type 0x08 subtype 0x00: 0x0000 0x0000 0x0000
Type: Transitive Flow spec redirect/mirror to IP next-hop (0x08)
0... .... = IANA Authority: Allocated on Standard Action
.0.. .... = Transitive across AS: Transitive
Subtype: 0x00
Raw Value: 0x0000 0x0000 0x0000
(…)

## Slide 25: Flowspec action Redirect to IP
qumran-flowspec#sh bgp flow-spec ipv4 deta
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3890478600
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Actions: Drop
qumran-flowspec#sh ip ro 112.112.112.112
(…)
S 112.112.112.112/32 [1/0] via 8.8.8.1, Ethernet5
qumran-flowspec#sh bgp flow-spec ipv4 det
(…)
Rule identifier: 3882061304
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 1 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 112.112.112.112
qumran-flowspec#sh flow-spec ipv4
(...)
Rule identifier: 3882061304
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Actions:
Redirect: VRF default, 112.112.112.112
Route via next hop 8.8.8.1
Status:
Installed: yes
Counter: 100005 packets
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
Scrubber
112.112.112.112/32

## Slide 26: Flowspec redirect VRF rule
Flowspec action EXTENDED_COMMUNITIES
Redirect to VRF
(…)
Path Attribute - EXTENDED_COMMUNITIES
Flags: 0xc0, Optional, Transitive, Complete
1... .... = Optional: Set
.1.. .... = Transitive: Set
..0. .... = Partial: Not set
...0 .... = Extended-Length: Not set
.... 0000 = Unused: 0x0
Type Code: EXTENDED_COMMUNITIES (16)
Length: 8
Carried extended communities: (1 community)
Flow spec redirect AS 2 bytes: RT 11:11 [Transitive Experimental]
Type: Transitive Experimental (0x80)
1... .... = IANA Authority: Allocated on First Come
.0.. .... = Transitive across AS: Transitive
Subtype (Experimental): Flow spec redirect AS 2 bytes (0x08)
2-Octet AS: 11
4-Octet AN: 11
(…)

## Slide 27: Flowspec action Redirect to VRF
qumran-flowspec#sh bgp flow-spec ipv4 deta
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3890478600
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Actions: Drop
qumran-flowspec(config)#sh bgp flow-spec ipv4 det
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3882114952
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 1 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric -, localpref 100, weight 0, valid, external, best
Actions: Redirect VRF: 11:11 (flow1)
qumran-flowspec(config)#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3882114952
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Actions:
Redirect: VRF flow1
Route via next hop 172.16.1.1
Status:
Installed: yes
Counter: 83565 packets
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
VRF
flow1

## Slide 28: Flowspec Operation Gotchas

## Slide 29: 1) Overlapping Flowspec Rules
Rules can be overlapping like ACL
However the main difference between static ACL and Flowspec is that there are no sequence order for Flowspec rules
Flowspec rules order/precedence instead based on its content
From RFC5575 Section 5.1
    (…)
    With traffic filtering rules, more than one rule may match a particular traffic flow. Thus, it is necessary to define the order at which rules get matched and applied to a particular traffic flow. This ordering function must be such that it must not depend on the arrival order of the flow specification's rules and must be constant in the network. The relative order of two flow specification rules is determined by comparing their respective components
    (…)
    For IP prefix values (IP destination and source prefix) precedence is given to the lowest IP value of the common prefix length; if the common prefix is equal, then the most specific prefix has precedence.
    (…)

## Slide 30: Overlapping Flowspec Rule example
Controller #1 (192.168.0.68) advertise rule to the Flowspec Router
In brief aggregated rule that focus more on a ill-behaved /32 source…
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
Controller
192.168.0.68
Actions: Drop
(…)
19:01:55 | 1366 | configuration | > neighbor | '192.168.0.111'
19:01:55 | 1366 | configuration | . local-as | '64515'
19:01:55 | 1366 | configuration | . peer-as | '1111'
19:01:55 | 1366 | configuration | . hold-time | '180'
19:01:55 | 1366 | configuration | > family |
19:01:55 | 1366 | configuration | . ipv4 | 'flow'
19:01:55 | 1366 | configuration | < family |
19:01:55 | 1366 | configuration | . router-id | '192.168.0.68'
19:01:55 | 1366 | configuration | . local-address | '192.168.0.68'
19:01:55 | 1366 | configuration | > flow |
19:01:55 | 1366 | configuration | > route |
19:01:55 | 1366 | configuration | > match |
19:01:55 | 1366 | configuration | . source | '11.11.11.1/32'
19:01:55 | 1366 | configuration | < match |
19:01:55 | 1366 | configuration | > then |
19:01:55 | 1366 | configuration | . discard |
(…)

## Slide 31: Overlapping Flowspec Rules…
Rule 3882099776 Installed in the Loc-RIB and in the TCAM
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
Controller
192.168.0.68
Actions: Drop
qumran-flowspec#sh bgp flow-spec ipv4 det
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for *;11.11.11.1/32;
Rule identifier: 3882099776
Matching Rule:
Destination Prefix: *
Source Prefix: 11.11.11.1/32
Paths: 1 available
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Drop
qumran-flowspec#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: *;11.11.11.1/32;
Rule identifier: 3882099776
Matches:
Source prefix: 11.11.11.1/32
Actions:
Drop
Status:
Installed: yes
Counter: 14 packets <==

## Slide 32: Overlapping Flowspec Rules…
More specific rule from Controller #2 (192.168.0.68) advertisment
In brief match both source and destination (for the same flow earlier) which means its more specific
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
Controller
192.168.0.68
qumran-flowspec#sh bgp flow-spec ipv4 deta
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3890478600
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Actions: Drop
(…)
19:03:55 | 1391 | configuration | > neighbor | '192.168.0.111'
19:03:55 | 1391 | configuration | . local-as | '64515'
19:03:55 | 1391 | configuration | . peer-as | '1111'
19:03:55 | 1391 | configuration | . hold-time | '180'
19:03:55 | 1391 | configuration | > family |
19:03:55 | 1391 | configuration | . ipv4 | 'flow'
19:03:55 | 1391 | configuration | < family |
19:03:55 | 1391 | configuration | . router-id | '192.168.0.67'
19:03:55 | 1391 | configuration | . local-address | '192.168.0.67'
19:03:55 | 1391 | configuration | > flow |
19:03:55 | 1391 | configuration | > route |
19:03:55 | 1391 | configuration | > match |
19:03:55 | 1391 | configuration | . source | '11.11.11.1/32'
19:03:55 | 1391 | configuration | . destination | '10.10.10.1/32'
19:03:55 | 1391 | configuration | < match |
19:03:55 | 1391 | configuration | > then |
19:03:55 | 1391 | configuration | . discard |
(…)

## Slide 33: Overlapping Flowspec Rules…
Since its two different rules with the same source (however different destinations), there are no BGP path-selection
Both installed in the Loc-RIB
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
Controller
192.168.0.68
qumran-flowspec#sh bgp flow-spec ipv4 deta
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3890478600
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Actions: Drop
qumran-flowspec#sh bgp flow-spec ipv4 det
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3882103864
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 1 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Drop
BGP Flow Specification Matching Rule for *;11.11.11.1/32;
Rule identifier: 3882099776
Matching Rule:
Destination Prefix: *
Source Prefix: 11.11.11.1/32
Paths: 1 available
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Drop

## Slide 34: Overlapping Flowspec Rules…
Note the flow itself have not changed
  (Src 11.11.11.1/32 and Dst 10.10.10.1/32)
However the counter now only active and increase only for the more specific flow rule 3882103864
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.67
Controller
192.168.0.68
qumran-flowspec#sh bgp flow-spec ipv4 deta
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3890478600
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Actions: Drop
qumran-flowspec#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3882103864
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Actions:
Drop
Status:
Installed: yes
Counter: 56 packets <==
Flow-spec rule: *;11.11.11.1/32;
Rule identifier: 3882099776
Matches:
Source prefix: 11.11.11.1/32
Actions:
Drop
Status:
Installed: yes
Counter: 0 packets <==

## Slide 35: 2) Flowspec=BGP (thereby Path-selection)
This is a realistic scenario and needs attention !
  Controllers can be synced and multiple just for redundancy.
  Or simple run individually (example have different detection data thereby different mitigation)
The Rule selection is secondary here, the selection based on the NLRI and BGP attributes
NOTE: Flowspec NLRI have no NEXT_HOP value to consider
  Thereby controllers that handle Flowspec Rules relative unaware of Routing logic, unless they also participate in the routing and receive complete RIB (ADD-PATH Clients)
Internet
Customer
Network/DC
10.10.10.0/24
10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Internet
10.10.10.1/32
(Good traffic)
Controller/Scrubber
Controller/Scrubber

## Slide 36: Flowspec=BGP => Path-selection…
DDoS flow is 11.11.11.1/32>10.10.10.1/32
  Controller .68 sends Rule with action Drop
  Controller .67 sends Rule with action Redirect
Path-selection => redirect win due to ORIGINATOR/ ROUTER_ID tie-breaker
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Internet
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good traffic)
Controller
192.168.0.67
Controller
192.168.0.68
qumran-flowspec#sh bgp flow-spec ipv4 deta
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3890478600
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Actions: Drop
qumran-flowspec#sh bgp flow-spec ipv4 detail
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3883141696
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Not best: Originator/Router ID
Actions: Drop

## Slide 37: Flowspec = BGP => Path-selection…
The actual Flowspec rule installed in the TCAM apply redirect action
Obviously BGP path-selection needs attention regards controllers and their BGP attribute(s) since in real life probably the scenario is the opposite
  First try to redirect
  Second (if volume to large to scrub) drop
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Internet
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good traffic)
Controller
192.168.0.67
Controller
192.168.0.68
qumran-flowspec#sh bgp flow-spec ipv4 deta
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3890478600
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
Paths: 2 available
64515
from 192.168.0.67 (192.168.0.67)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Redirect IP: 8.8.8.1
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external
Actions: Drop
qumran-flowspec#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;
Rule identifier: 3883141696
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Actions:
Redirect: VRF default, 8.8.8.1
Route via next hop 8.8.8.1
Status:
Installed: yes
Counter: 0 packets
Scrubber
8.8.8.1

## Slide 38: Flowspec Rule error example
Controller ship rule to the Router
NOTE: The rule is by purpose a weirdo…
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.68
Actions: Drop
20:02:37 | 2354 | configuration | > neighbor | '192.168.0.111'
20:02:37 | 2354 | configuration | . local-as | '64515'
20:02:37 | 2354 | configuration | . peer-as | '1111'
20:02:37 | 2354 | configuration | . hold-time | '180'
20:02:37 | 2354 | configuration | > family |
20:02:37 | 2354 | configuration | . ipv4 | 'flow'
20:02:37 | 2354 | configuration | < family |
20:02:37 | 2354 | configuration | . router-id | '192.168.0.68'
20:02:37 | 2354 | configuration | . local-address | '192.168.0.68'
20:02:37 | 2354 | configuration | > flow |
20:02:37 | 2354 | configuration | > route |
20:02:37 | 2354 | configuration | > match |
20:02:37 | 2354 | configuration | . source | '11.11.11.1/32'
20:02:37 | 2354 | configuration | . destination | '10.10.10.1/32'
20:02:37 | 2354 | configuration | . destination-port | '=80&>8080&<8088'
20:02:37 | 2354 | configuration | . source-port | '>=1024'
20:02:37 | 2354 | configuration | . protocol | '=tcp'
20:02:37 | 2354 | configuration | < match |
20:02:37 | 2354 | configuration | > then |
20:02:37 | 2354 | configuration | . discard |
20:02:37 | 2354 | configuration | < neighbor |

## Slide 39: Flowspec Rules error…
The BGP RIB accepts the rule
The reason for acceptance is based on the RFC where BGP part (RIB) only suppose to check BGP and the route Validation function
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.68
Actions: Drop
qumran-flowspec#sh bgp flow-spec ipv4 det
BGP Flow Specification rules for VRF default
Router identifier 111.111.111.111, local AS number 1111
BGP Flow Specification Matching Rule for 10.10.10.1/32;11.11.11.1/32;IP:=6;DP:=80&>8080&<8088;SP:>=1024;
Rule identifier: 3882110944
Matching Rule:
Destination Prefix: 10.10.10.1/32
Source Prefix: 11.11.11.1/32
IP Protocol: =6
Destination Port: =80 & >8080 & <8088
Source Port: >=1024
Paths: 1 available
64515
from 192.168.0.68 (192.168.0.68)
Origin IGP, metric 111, localpref 100, weight 0, valid, external, best
Actions: Drop

## Slide 40: Flowspec Rules error…
However the TCAM FIB do not accept the rule (since its false)
  Dst port equal to 80 and needs to be between 8080-8088 !!!
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.68
Actions: Drop
qumran-flowspec#sh flow-spec ipv4 infeasible
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;IP:=6;DP:=80&>8080&<8088;SP:>=1024;
Rule identifier: 3882110944
Infeasible due to Destination port
Status:
Installed: no(infeasible rule)

## Slide 41: 3) Flowspec Rule scale and TCAM
Controller ship rule to the Router
NOTE: The rule simple Src IP with action drop
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.68
Actions: Drop
(…)
21:29:17 | 2521 | configuration | > neighbor | '192.168.0.111'
21:29:17 | 2521 | configuration | . local-as | '64515'
21:29:17 | 2521 | configuration | . peer-as | '1111'
21:29:17 | 2521 | configuration | . hold-time | '180'
21:29:17 | 2521 | configuration | > family |
21:29:17 | 2521 | configuration | . ipv4 | 'flow'
21:29:17 | 2521 | configuration | < family |
21:29:17 | 2521 | configuration | . router-id | '192.168.0.68'
21:29:17 | 2521 | configuration | . local-address | '192.168.0.68'
21:29:17 | 2521 | configuration | > flow |
21:29:17 | 2521 | configuration | > route |
21:29:17 | 2521 | configuration | > match |
21:29:17 | 2521 | configuration | . source | '11.11.11.1/32'
21:29:17 | 2521 | configuration | < match |
21:29:17 | 2521 | configuration | > then |
21:29:17 | 2521 | configuration | . discard |
(…)

## Slide 42: Flowspec Rule scale and TCAM…
TCAM FIB accept the rule and install
TCAM space consume 1 entry of 24576
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.68
Actions: Drop
qumran-flowspec#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: *;11.11.11.1/32;
Rule identifier: 3882112096
Matches:
Source prefix: 11.11.11.1/32
Actions:
Drop
Status:
Installed: yes
Counter: 0 packets
qumran-flowspec#sh hardware capacity | grep Flowspec
TCAM Flowspec Jericho0 1 0% 24575 2048 24576 2

## Slide 43: Flowspec Rule scale and TCAM…
Controller update the rule to the Router
NOTE: The rule “verbose” format
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.68
Actions: Drop
(…)
21:34:56 | 2536 | configuration | > neighbor | '192.168.0.111'
21:34:56 | 2536 | configuration | . local-as | '64515'
21:34:56 | 2536 | configuration | . peer-as | '1111'
21:34:56 | 2536 | configuration | . hold-time | '180'
21:34:56 | 2536 | configuration | > family |
21:34:56 | 2536 | configuration | . ipv4 | 'flow'
21:34:56 | 2536 | configuration | < family |
21:34:56 | 2536 | configuration | . router-id | '192.168.0.68'
21:34:56 | 2536 | configuration | . local-address | '192.168.0.68'
21:34:56 | 2536 | configuration | > flow |
21:34:56 | 2536 | configuration | > route |
21:34:56 | 2536 | configuration | > match |
21:34:56 | 2536 | configuration | . source | '11.11.11.1/32'
21:34:56 | 2536 | configuration | . destination | '10.10.10.1/32'
21:34:56 | 2536 | configuration | . destination-port | '[' '=80' '>8080&<8088' ']'
21:34:56 | 2536 | configuration | . source-port | '>=1024'
21:34:56 | 2536 | configuration | . protocol | '=tcp'
21:34:56 | 2536 | configuration | < match |
21:34:56 | 2536 | configuration | > then |
21:34:56 | 2536 | configuration | . discard |
(…)

## Slide 44: Flowspec Rules and TCAM…
TCAM FIB accept the rule and install
The single rule consume 2 entries of 24576 TCAM space since more complex
Internet
Customer
Network/DC
10.10.10.0/24
Src 11.11.11.1/32
Dst 10.10.10.1/32
(Good and Bad traffic)
Operator
Core
Controller
192.168.0.68
Actions: Drop
qumran-flowspec#sh flow-spec ipv4
Flow specification rules for VRF default
Applied on: Ethernet7
Flow-spec rule: 10.10.10.1/32;11.11.11.1/32;IP:=6;DP:=80|>8080&<8088;SP:>=1024;
Rule identifier: 3882110920
Matches:
Destination prefix: 10.10.10.1/32
Source prefix: 11.11.11.1/32
Next protocol: 6
Destination port: 80
8081-8087
Source port: 1024-65535
Actions:
Drop
Status:
Installed: yes
Counter: 0 packets
qumran-flowspec#sh hardware capacity | grep Flowspec
TCAM Flowspec Jericho0 2 0% 24574 2048 24576 2

## Slide 45: Questions