## Slide 1: EVPN VPWS The “new” standard for E-line
Peter Lundqvist
SE Manager Arista Nordics

## Slide 2: EVPN VPWS Agenda
Why Layer 2 Services?
  Where did it start ?
EVPN VPWS Service&Theory
  L2 rarely work, except if its over BGP
EVPN VPWS FXC
  Lets scale it, OAM challange
ECMP with MPLS VPN
  That weird thing and its solution (Flow labels)
EVPN VPWS Sample
  PW => VPWS

## Slide 3: Why Layer 2 Services?

## Slide 4: MPLS Layer 2 VPN Services Overview
There are many types:
  Layer 2 (p2p, p2mp, mp2mp) services
  Multicast Services
  Layer 3 services
Layer 2 VPN
  VPLS/EVPN (E-LAN) and Pseudowire (E-Line) Services
  BGP based services
    EVPN and Variants of VPLS/PW are BGP based
  LDP Based services
    Pseudowire/ VPLS
Why Layer 2 VPN?
  Stretch Layer 2
  Enterprise – Layer 2 stretch for application/VLAN
  SP (revenue) – Layer 2 transparent services to customers

## Slide 5: Where did it start
“There are many types…”
Perhaps needed, but honestly mucho politics going on between vendors
Customers pain to solve the vendor interopability
Learning and rollout based on hard learn lesson(s)…
Question
How can two brothers with wuch high IQ (and with the same mother), come up with two different solutions that solve(s) very much the same thing(s) ???
MPLS VPN
L2VPN
L3VPN
4364/2547
E-Lan
E-Line
Martini
RFC4447
Kompella
RFC6624
VPLS BGP
RFC4761
VPLS LDP
RFC4762

## Slide 6: EVPN – The All-in-One Address Family
Standards Based - Open Standards for Inter-operation
Flexible Service Types – E-Line/E-LAN & IP VPN Services
Universal BGP Control Plane – Simplify, Standardize
Scalable – BGP Based Scalable VPN Services
Secure – MAC Mobility, ARP Suppression, Policy Control
Efficient – Multi-Homing Support, A/A Forwarding, Scaled ECMP
Supports Different Encapsulation Types – IP VXLAN & MPLS
EVPN
DC L3SL DCI
Edge VPN Services
IX
WAN
Metro Ethernet

## Slide 7: EVPN VPWS Services

## Slide 8: EVPN Main Standards Summary
EVPN Standards RFC 7432, RFC 8214 (VPWS), Draft for VPWS-FXC
  Previously known as draft-ietf-l2vpn-evpn
  Specifics an BGP EVPN control plane with a MPLS data plane
  BGP control plane
    One address family to signal services and advertise MAC, MAC/IP and IP prefixes.
  Multi-vendor authors involving vendors and operators :
    ALU, Cisco, Juniper, AT&T, Bloomberg and Verizon
EVPN Standard RFC 8365 – Network Virtualization Overlay
  Same EVPN control plane with IP (VXLAN) Data plane
EVPN MP-BGP
RFC 7432
Control
Plane
Data
Plane
MPLS
RFC 7432
Network Virtualization Overlay (NVO)
NVGRE, VXLAN, Implore
    RFC8365
Provider Backbone Bridging (PBB)
    Draft-ietfl-l2evpn-pbb-evpn
EVPN VPWS
RFC 8214
EVPN VPWS-FXC
    draft-ietf-bess-evpn-vpws-fxc-00

## Slide 9: Benefits of EVPN VPWS Services vs LDP
Active- PE
Active-PE
EVI
EVI
Active- PE
EVI
EVI
Multi-node Active-Active Site
MPLS CORE
LDP/ISIS-SR/BGP-SR
Ethernet Segment A
Active-Active Multi-homing
  Flow based A/A forwarding
BGP Control Plane
  Standardize, Interoperable, Scalable
  No separate control protocol for PW signaling (LDP)
  Can use BGP fast convergence techniques
Efficient
  Multi-Homing Support with A/A Forwarding
  Fast convergence (Mass withdrawal)
  Scaled ECMP
Flexible
  Inter-AS deployments (BGP)
  BGP-based control plane provides ability to apply fine-grained policies
DF
  L2 rarely work, unless its based on BGP 

## Slide 10: EVPN VPWS Terminology
MPLS
Active PE 3
Active PE 4
Active PE 2
Active PE 1
EVI A
Ethernet Segment A
(Multi-homed Site A)
ESI 00:11:11:11:11:11:11
Ethernet Segment B
(Multi-homed Site B)
ESI 00:22:22:22:22:22:22
CE1
CE2
EVI A
EVI A
EVI A
Local Layer 2
MP-iBGP/eBGP EVPN
Local Layer 2
P
P
P
DF
DF
H1
M1
H2
M2
VPWS 101
VPWS 101
VPWS 202
VPWS 202
Attachment circuit (AC)
EVPN VPWS Instance (EVI)

## Slide 11: EVPN VPWS Supported Topologies
Active- PE
Active-PE
EVI
EVI
Active- PE
EVI
EVI
Multi-node Active-Active Site
Ethernet Segment A
Active- PE
EVI
Single-Node Site
Ethernet Segment A
Dot1q Trunk
Dot1q Trunk
(Port-Channel)
Dot1q Trunk
(Port-Channel)
Active- PE
Active-PE
EVI
EVI
Active- PE
EVI
EVI
Multi-node Active-Standby Site
Ethernet Segment A
DF
BDF
NDF
MPLS CORE
LDP/ISIS-SR/BGP-SR

## Slide 12: EVPN VPWS Types – VLAN Based Service
EVI-1
Eth1
(VLAN 10)
EVI-1 (2 Labels)
Eth 3
(VLAN 11)
EVI-2 (2 Labels)
RD-1, RT-1
EVPN VPWS service instance (EVI) is represented by a pair of downstream assigned EVPN service labels associated with a pair of endpoints
VPWS ID 10
EVI-2
RD-2, RT-2
VPWS ID 11
EVI-2
VPWS ID 13
RD-4, RT-2
EVI-1
VPWS ID 12
RD-3, RT-1
Eth 2
(VLAN 11)
Eth 4
(VLAN 10)
Single VLAN on Specific Port → 1:1 Mapping of VPWS ID to VLAN ID
PE Provides x-connect between <PORT,VLAN> and VPN Label
VPN Label Identified by local PORT,VLAN and VPWS ID
Original VLAN ID SHOULD Remain on Eth Frame Over MPLS (QOS transparency)
If VLAN Translation required MUST be performed on Egress PE

## Slide 13: EVPN VPWS Types – VLAN Bundle Service
EVI-1
EVI-1
Eth 1
(VLAN 10)
EVI Label + Ethernet tag
RD-1, RT-1
VPWS ID 11
RD-3, RT-1
Eth 1
(VLAN 11)
Eth2
(VLAN 10)
Eth 2
(VLAN11)
Ethernet Tag retained in encapsulated frame. Only the EVI label only identifies the VPWS
VPWS ID 12
EVPN VPWS service instance (EVI) is represented by a pair of downstream assigned EVPN service labels associated with a pair of endpoints
Group of VLANs on Specific Port → 1:N Mapping of VPWS ID to NxVLAN IDs
Transmitting PE Provides x-connect between <PORT,N x VLAN > and VPN Label
Receiving PE x-connect based on VPN Label alone → Egress Port
Original VLAN ID MUST Remain on Eth Frame (Single VLAN ID only)
No VLAN Translation Allowed

## Slide 14: EVPN VPWS Types – Port Based Service
EVI-1
EVI-1
Eth 1
(ALL VLANs)
EVI Label + Ethernet tag
RD-1, RT-1
VPWS ID 11
RD-3, RT-1
Eth 2
(ALL VLANs)
Ethernet Tag retained in
encapsulated frame
VPWS ID 12
EVPN VPWS service instance (EVI) is represented by a pair of downstream assigned EVPN service labels associated with a pair of endpoints
All VLANs on Specific Port
All VLANs Mapped to VPWS ID
Rest of Behaviour Identical to Bundle Service

## Slide 15: EVPN VPWS EVPN Route Types theory

## Slide 16: BGP EVPN Main Route Types
Route Type | Description
1 | Auto-Discover (A-D) Segment route – A/A multi-homing forwarding, and allow remote discovery of dual-homed Segments.
2 | MAC address Route - Advertisement of locally learnt/provisioned MAC address and optionally IP addresses.
3 | Inclusive Multicast Ethernet Route - For advertisement EVI membership for the creation of ingress replication lists
4 | Ethernet Segment Route – For multi-homing deployments to allow Peer discovery on same segment and DF election
5 | IP prefix Route, advertisement of a IP prefix and next-hop, no MAC address for the route is advertised.

## Slide 17: EVPN VPWS Relevant Route Types
Route Type | Description
1 | Auto-Discover (A-D) Segment route – Per-EVI Ethernet A-D route signal VPWS services and A/A multi-homing
2 | MAC address Route - Advertisement of locally learnt/provisioned MAC address and optionally IP addresses.
3 | Inclusive Multicast Ethernet Route - For advertisement EVI membership for the creation of ingress replication lists
4 | Ethernet Segment Route – For multi-homing deployments to allow Peer discovery on same segment and DF election
5 | IP prefix Route, advertisement of a IP prefix and next-hop, no MAC address for the route is advertised.
Enabled With The Following Route Type:
Type 1 – Auto-Discover Segment route
Type 4 – Ethernet Segment Route For Designated Forwarder Election

## Slide 18: Multi-homed Sites Using LAG The Concepts of ES and ESI
PE1
CE
PE2
LAG
LAG
Ethernet Segment Identifier (ESI)
10 bytes (e.g. 00:11:11:11:11:11:11:11:11:11)
Operator Assigned ESI (Must start with 00
Ethernet Segment (ES)
Set of links connected to same “customer site/host”
Links can be Single-Active or All-Active
CE
A/A
Ethernet Segment
A/S
Ethernet Segment

## Slide 19: Route Types – Type 1 (EVPN VPWS)
  Type 1 EVPN route – The Auto-Discover Per-EVI Route
  Type-1 per-EVI used for VPWS signaling
Type 1 NLRI
Next-hop for the prefixes within the NLRI
= IP of the advertising PE
Route Target Ext Community
Route Distinguisher (RD)
Ethernet Segment Identifier = <value>
Ethernet Tag ID = VPWS ID
MPLS Label (EVI label)
Standard type-1 RD <IP Address>:<ID>. Identifies a MAC VRF
Set to the ESI value configured (10 octet)
label for EVI. Downstream assigned
Route Type ( A-D Route, Type 1)
Length
1 - Ethernet A-D Route
2 - MAC-advertisement Route
3 - Inclusive Multicast Route
4 - Ethernet Segment Route
5 - IP prefix route (optional)
Set to the VPWS ID. Value up to 24 bits, right aligned
Route target for the EVI
Layer 2 EVPN Ext Community
EVPN VPWS Specific information
Layer 2 EVPN Ext Community
Type (0x06) / Sub-type (0x04) (2 octets)
Control Flags (2 octets)
L2 MTU (2 octets)
Reserved (2 octets)
MTU value to be negotiated. Non zero value must match.
Type/Sub type identifier
Control Flags
Must be 0 (13 bits)
P (1 bit)
B (1 bit)
C (1 bit)
All PEs set to 1 in A/A MH
Primary PE sets 1 for A/S MH
Set to 1 on backup PEs in A/S MH
If set to 1 CW MUST be present
Path Attribute MP_REACH_NLRI NEXT_HOP = PE IP AFI = 25 (L2VPN) , SAFI =70 (EVPN)
Notes: MP_REACH_NLRI Path Attribute. Optional and Transitive

## Slide 20: Ethernet Auto-Discovery (Type 1) Route Per Ethernet Segment (ES): Mass Withdraw&Active Active Multi-Homing Signaling
NLRI | Route type | Ethernet Auto-Discovery Route (Type 1)
 | Route Distinguisher (RD) | RD of EVI on PE2
 | Ethernet Segment ID (ESI) | 0:1:1:1:1:1:1:1:1:1
 | Ethernet Tag ID | FF..
 | MPLS label | 0
Extended communities |  | ESI Label Extended Community: Single-Active Flag = false (0) ESI Label = 300
Next-hop |  | Loopback IP address of PE2
Other attributes (Origin, AS-PATH, LOCAL_PREF …) |  | 
PE3
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE2
PE1
CE2
MPLS
MP-BGP
RR
Ethernet AD per-ES (Type 1) Route for ESI 0:1:1:1:1:1:1:1:1:1, ALL RTs in ESI, ESI Label 300, SA Flag = 0

## Slide 21: Ethernet Auto-Discovery (Type 1) EVPN VPWS Routes Per Ethernet Virtual Instance (EVI): VPWS Signaling (Active Active)
NLRI | Route type | Ethernet Auto-Discovery Route (Type 1)
 | Route Distinguisher (RD) | RD of EVI on PE2
 | Ethernet Segment ID (ESI) | 0:1:1:1:1:1:1:1:1:1
 | Ethernet Tag ID | 100 (VPWS ID)
 | MPLS label | 500
Extended communities |  | RT Extended Community Layer 2 EVPN Ext Community: Primary PE =1
Next-hop |  | Loopback IP address of PE2
Other attributes (Origin, AS-PATH, LOCAL_PREF…) |  | 
PE3
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE2
PE1
CE2
MPLS
MP-BGP
RR
Ethernet AD per-EVI (Type 1) Route for ESI 0:1:1:1:1:1:1:1:1:1, RT for EVI, ETID 100, Label 500, P 1

## Slide 22: Ethernet Auto-Discovery (Type 1) EVPN VPWS Routes Per Ethernet Virtual Instance (EVI): VPWS Signaling (Single Homed)
NLRI | Route type | Ethernet Auto-Discovery Route (Type 1)
 | Route Distinguisher (RD) | RD of EVI on PE1
 | Ethernet Segment ID (ESI) | 0
 | Ethernet Tag ID | 100 (VPWS ID)
 | MPLS label | 600
Extended communities |  | RT Extended Community Layer 2 EVPN Ext Community: 9000 L2 MTU (optional)
Next-hop |  | Loopback IP address of PE1
Other attributes (Origin, AS-PATH, LOCAL_PREF, …) |  | 
Ethernet AD per-EVI (Type 1) Route for ESI 0, RT for EVI, ETID 100, Label 600, MTU 9000
PE3
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE2
PE1
CE2
MPLS
MP-BGP
RR

## Slide 23: Mass Withdrawal Operation
Connection between PE3 and CE2 goes down
PE3 first withdraws route for ESI before withdrawing all Ethernet A-D per EVI routes
When PE1 sees that ESI is withdrawn, it flushes all routes on that ESI from the FIB
2
    Withdraw Ethernet AD per-ES (type-1) Route for ESI
3
1
PE2
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE3
PE1
CE2
MPLS
MP-BGP
RR
VLAN 100
VLAN 101
VLAN 102
VLAN 103
VLAN 1000
❌
Trunk VLANs 100 → 1000 (900 VLAN based VPWS IDs)
VLAN 100
VLAN 101
VLAN 102
VLAN 103
VLAN 1000
Trunk VLANs 100 → 1000 (900 VLAN based VPWS IDs)
    Withdraw Ethernet AD per-EVI (Type 1) Route for VPWS ID 1000
…
    Withdraw Ethernet AD per-EVI (Type 1) Route for VPWS ID 100
    Withdraw Ethernet AD per-EVI (Type 1) Route for VPWS ID 101

## Slide 24: EVPN VPWS: Active-Active Multi-homing.
  EVPN VPWS A/A Forwarding Overview
  All PEs set Control Flag ”P”
  No Designated Forwarder Election
  All Active PEs forward traffic
MPLS
Active- PE
Active- PE
Active- PE
Active- PE
Ethernet Segment A
Ethernet Segment B
EVI
CE1
CE2
Traffic Flow
EVI
EVI
EVI
VPWS 101
VPWS 100

## Slide 25: Active/Active EVPN VPWS Forwarding Plane
PE1 receives both Ethernet Auto-Discovery (type 1) Routes from PE2
PE1 receives both Ethernet Auto-Discovery (type 1) Routes from PE3
PE1 Installs both Remote PEs in the forwarding table.
PE1 Imposes the VPWS Label (400,300) and Transport labels 900002 and 900003 for PE2 and PE3 respectively
2
PE2
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE3
PE1
CE2
MPLS
MP-BGP
RR
4
Ethernet AD per-EVI (Type 1) Route for ESI 0, RT for EVI, ETID 100, Label 400, P = 1
Ethernet AD per-EVI (Type 1) Route for ESI 0, RT for EVI, ETID 100, Label 300, P = 1
Ethernet AD per-ES (Type 1) Route for ESI 0:1:1:1:1:1:1:1:1:1, ALL RTs in ESI, ESI Label 200, SA Flag = 0
Ethernet AD per-ES (Type 1) Route for ESI 0:1:1:1:1:1:1:1:1:1, ALL RTs in ESI, ESI Label 200, SA Flag = 0
1
VLAN 100
VLAN 100
RIB |  |  | FIB
VPN | ESI | ETID | NH
RT | ESI | 100 | PE2/PE3
3

## Slide 26: EVPN VPWS: Active-Standby Multi-homing.
  EVPN VPWS A/S Forwarding Overview
  Run Designated Forwarder Election
  All Primary (DF) PEs set Control Flag ”P”
  Backup (BDF) Pes set the Control Flag “B”
  If more than 2 PEs in ES rest of PEs don’t set either flag (Non-DF)
MPLS
Active- PE
Standby-PE
Standby-PE
Active- PE
Ethernet Segment A
Ethernet Segment B
EVI
CE1
CE2
EVI
EVI
EVI
VPWS 100
✚
✚
Traffic Flow

## Slide 27: Why is a Designated Forwarder Required For Active Standby?
If not addressed:
      Assuming Flow load-balancing from PE1, half the traffic will be Lost!
PE2
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE3
PE1
CE2
MPLS
MP-BGP
RR
Send to Both PEs
DROP!
⚠️

## Slide 28: Route Types – Type 4 (EVPN VPWS)
  Type 4 EVPN route – The Ethernet Segment Route (ES)
  Used for DF Election
  Manually configure the ESI and ES-Import RT
    Type 0x0 ESI (operator assigned)
  Run a sequential modulo (MOD) operation for VPWS IDs (M) shared across N = Number of PEs in a site
  Carries the ES-Import RT Ext Community
    Only imported by PEs connected to same Ethernet Segment
    ES-Import RT derived from higher order 6 octets of 9 octet ESI in other vendors type 0x0 implementation
Type 4 NLRI
Next-hop for the prefixes within the NLRI
= IP of the advertising PE
ES-Import RT Extended Community
Route Distinguisher (RD)
Ethernet Segment Identifier = <value>
IP Address Length
IP Address
Type 1 RD (derived from <loopback IP>:1). Not used to identify VPN as per usual. Here it is used to identify the PE
Set to the ESI value configured
IP Address of the advertising PE
Route Type ( ES Route, Type 4)
Length
1 - Ethernet A-D Route
2 - MAC-advertisement Route
3 - Inclusive Multicast Route
4 - Ethernet Segment Route
5 - IP prefix route (optional)
IP Address length (1 byte)
Path Attribute MP_REACH_NLRI NEXT_HOP = PE IP AFI = 25 (L2VPN) , SAFI =70 (EVPN)
Notes: MP_REACH_NLRI Path Attribute. Optional and Transitive

## Slide 29: The Designated Forwarder Election
List of ESI PEs (lowest to highest IP) | DF Result of MOD Calculation
1.1.1.1 (0) | 0,3,6,9…....
2.2.2.2 (1) | 1,4,7,10…....
3.3.3.3 (2) | 2,5,8,11…....
For VPWS ID – MOD operation on VLAN 423 with N = 3 (PEs) MOD == 0
(so 1.1.1.1 is DF, 2.2.2.2 BDF, 3.3.3.3 Non DF)
PE1 1.1.1.1
ESI 0:1:1:1:1:1:1:1:1:1
PE2 2.2.2.2
CE
MP-BGP
PE1 3.3.3.3

## Slide 30: Designated Forwarder Operation to Active Standby ES Service Carving
  Result of the MOD operation elects PE2 as DF for VPWS ID 423 and PE3 as DF for VPWS ID 424, PE4 DF for VPWS ID 425
  Traffic is therefore load-balanced per VPWS ID to a remote A/S multi-homed Ethernet segment
PE2
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE4
PE1
CE2
MPLS
MP-BGP
RR
PE2 DF For EVI 423
PE3 DF For EVI 424
PE3
PE3 DF For EVI 425

## Slide 31: EVPN VPWS FXC Extensions to VPWS with Flexible Cross Connect

## Slide 32: Why EVPN VPWS FXC ? => Scale !!!
Significantly reduce number of PWs by multiplexing VLANs across many interfaces
Reduce BGP signaling as much as possible (e.g., not to signal every VLAN/AC)
Still maintain support for All-Active (LAG) and Single-Active multi-homing and mass MAC withdrawal, VLAN translation
https://tools.ietf.org/html/draft-ietf-bess-evpn-vpws-fxc-00
CE1000
32
32
CE2
VLAN 100
VLAN 1000
VLAN 100
VLAN 1000
VLAN 100
VLAN 1000
VLAN 100
VLAN 1000
PE2
ESI 0:1:1:1:1:1:1:1:1:1
CE1
PE3
PE1
MPLS
VLAN 100
VLAN 1000
VLAN 100
VLAN 1000
CE1
CE2
CE1000
VPWS ID 100
VPWS ID 200
Trunk VLANs 100 → 1000, 1000 CEs (900,000 VLANs, 1 VPWS ID)
Trunk VLANs 100 → 1000, 1000 CEs (900,000 VLANs, 1 VPWS ID)

## Slide 33: EVPN VPWS FXC Topologies Supported
  Point to Point
  (Most common)
  Point to Multi-point

## Slide 34: Challenges With VPWS FXC?
  Single VPWS service tunnel multiplexes many ACs across number of Ethernet Segments (number of physical interfaces) and therefore each ACs are not signaled via EVPN BGP to remote PE devices
  Remote PE devices do not know the association of the received Ethernet Segment to these ACs, or the association of the VPWS service tunnel/label. (the remote PEs only know the association of their local ACs to the VPWS service but not the far-end ACs).
  If ES failure is signaled via EVPN to the remote PE devices, they don't know what to do with such message because they don't know the association among the remote ES, the remote ACs, and the VPWS service tunnel.

## Slide 35: Solution to the Multiplexing Challenge
  VLAN “Normalization”
  Can have over-lapping VLANs with multiple ACs
  Need to map each local VLAN to a local “unique VLAN ID”
  If the the number of “Unique VLANs” > 4,000 then single to double TAG translations MUST be performed.
    Use the 24 bit VPWS ID (Eth TAG field in EVPN route) used to identify the unique normalized VLAN ID.
    Single Tag -> Lower 12bits
    Dual Tag -> Inner Tag lower 12bits : Outer Tag top 12 bits
    PEs must maintain mapping of Label (VRF) AND Normalized VLAN -> Egress VLAN and Port
  Define Two New Modes of Operation
  Signaled in the Control flag extensions in the Ethernet AD per EVI route
  VLAN Signaled FXC
  Default FXC

## Slide 36: Route Types – Type 1 (EVPN VPWS FXC)
  Type 1 EVPN route – The Auto-Discover Per-EVI Route (AD per-EVI)
  Two new OPTIONAL control fields to signal mode of operation M (00 – per RFC8214, 01 - VLAN signaled, 10 – Default FXC) and V (00 – per RFC8214, 01 – Single VID , 10 – Dual VID)
Path Attribute MP_REACH_NLRI NEXT_HOP = PE IP AFI = 25 (L2VPN) , SAFI =70 (EVPN)
Type 1 NLRI
Next-hop for the prefixes within the NLRI
= IP of the advertising PE
Route Target Ext Community
Route Distinguisher (RD)
Ethernet Segment Identifier = <value>
Ethernet Tag ID = VPWS ID
MPLS Label (EVI label)
Standard type-1 RD <IP Address>:<ID>. Identifies a MAC VRF
Set to the ESI value configured (10 octet)
label for EVI. Downstream assigned
Route Type ( A-D Route, Type 1)
Length
1 - Ethernet A-D Route
2 - MAC-advertisement Route
3 - Inclusive Multicast Route
4 - Ethernet Segment Route
5 - IP prefix route (optional)
Set to the VPWS ID. Value up to 24 bits, right aligned
Route target for the EVI
Layer 2 EVPN Ext Community
EVPN VPWS Specific information
Layer 2 EVPN Ext Community
Type (0x06) / Sub-type (0x04) (2 octets)
Control Flags (2 octets)
L2 MTU (2 octets)
Reserved (2 octets)
MTU value to be negotiated. Non zero value must match.
Type/Sub type identifier
Control Flags
Must be 0 (13 bits)
V (1 bit)
M (1 bit)
C (1 bit)
P (1 bit)
B (1 bit)
All PEs set to 1 in A/A MH
Primary PE sets 1 for A/S MH
Set to 1 on backup PEs in A/S MH
If set to 1 CW MUST be present
Mode of operation
Normalized VLAN Single or Dual Tag
Notes: MP_REACH_NLRI Path Attribute. Optional and Transitive

## Slide 37: EVPN VPWS FXC Modes of Operation VLAN-Signaled Mode
  One of the end points are Multi—Homed CEs (VLAN-Signaled Flexible Xconnect (M = 10))
  Now single tunnel represented by MANY VPWS IDs
            Normalized VLAN IDs ARE signaled in BGP EVPN
            PEs signal the VLANs (normalized VIDs (N-VIDs)) in EVPN BGP
            Ethernet AD per EVI route is sent for each VID (i.e. normalized VID)
Ethernet AD per-EVI (Type 1) Route for ESI ESI 0:2:2:2:2:2:2:2:2:2, RT for EVI, ETID 2, Label 600, M 10, V 01
VLAN 1
VLAN 2
VLAN 1
VLAN 2
CE1
CE2
ESI 0:2:2:2:2:2:2:2:2:2
PE2
PE3
PE1
MPLS
VPWS ID 100
VPWS ID 200
ESI 0:1:1:1:1:1:1:1:1:1
VLAN 1
VLAN 2
VLAN 1
VLAN 2
CE1
CE2
Ethernet AD per-EVI (Type 1) Route for ESI ESI 0:2:2:2:2:2:2:2:2:2, RT for EVI, ETID 1, Label 600, M 10, V 01

## Slide 38: EVPN VPWS FXC Modes of Operation Default Mode
  Single Homed CEs (DEFAULT Flexible Xconnect (M = 01))
  No signal of each AC in BGP
            Failure of ES (single homed) will be detected
            PEs do not need to signal the VLANs (normalized VIDs) in EVPN BGP
            In this solution, there is only a single P2P EVPN VPWS service tunnel between a pair of PEs for a set of ACs
            A single Ethernet AD per EVI route is sent upon configuration of the first AC (i.e. normalized VID)
            Additional AC configured for this VPWS do NOT generate any further BGP EVPN routes
Ethernet AD per-EVI (Type 1) Route for ESI 0, RT for EVI, ETID 100, Label 600, M 10, V 01
PE2
PE1
MPLS
VLAN 100
VLAN 1000
VLAN 100
VLAN 1000
CE1
CE2
VPWS ID 100
VLAN 100
VLAN 1000
VLAN 100
VLAN 1000
CE1
CE2

## Slide 39: EVPN VPWS OAM Failure Scenarios

## Slide 40: EVPN VPWS FXC Failure Scenarios Port Failure : VLAN-Signaled Mode
Port failure ETH1 (between PE3 and CE1)
Triggers PE3 to signal an AD per-ES withdrawal for ES to CE1
Triggers PE3 to signal an AD per-EVI withdrawal for ETH1:V1 -> normalized VID *1 & ETH1:V2 -> normalized VID *2
PE1 Removes PE3 from the forwarding list for VID 1 and VID2
2
Withdraw Ethernet AD per-EVI (Type 1) Route for ESI 0:2:2:2:2:2:2:2:2, RT for EVI, ETID 1, Label 200, P = 1, V = 01, M = 01
1
VLAN 1
VLAN 2
VLAN 1
VLAN 3
CE1
CE2
ESI 0:2:2:2:2:2:2:2:2:2
PE2
PE3
PE1
MPLS
VPWS ID 100
VPWS ID 200
ESI 0:1:1:1:1:1:1:1:1:1
VLAN 1
VLAN 2
VLAN 1
VLAN 3
CE1
CE2
❌
ETH1
ETH2
RIB |  |  | FIB
VPN | ESI | ETID | NH
RT | ESI | 1 | PE2/PE3
RT | ESI | 2 | PE2/PE3
❌
4
Withdraw Ethernet AD per-EVI (Type 1) Route for ESI 0:2:2:2:2:2:2:2:2, RT for EVI, ETID 2, Label 200, P = 1, V = 01, M = 01
❌
Withdraw Ethernet AD per-ES (Type 1) Route for ESI 0:2:2:2:2:2:2:2:2:2, ALL RTs in ESI, ESI Label 400, SA Flag = 0
3

## Slide 41: EVPN VPWS FXC Failure Scenarios Port Failure : Default Mode
Port failure ETH1 (between PE3 and CE1)
Triggers PE3 to signal an AD per-EVI withdrawal for ETH1
PE1 Removes PE3 from the forwarding list for VID 1 and VID2
1
VLAN 1
VLAN 2
VLAN 1
VLAN 3
CE1
CE2
ESI 0:2:2:2:2:2:2:2:2:2
PE2
PE3
PE1
MPLS
ESI 0:1:1:1:1:1:1:1:1:1
VLAN 1
VLAN 2
VLAN 1
VLAN 3
CE1
CE2
❌
ETH1
ETH2
VPWS ID 100
VPWS ID 200
VPWS ID 300
VPWS ID 400
RIB |  |  | FIB
VPN | ESI | ETID | NH
RT | ESI | 1 | PE2/PE3
RT | ESI | 2 | PE2/PE3
❌
❌
3
Withdraw Ethernet AD per-EVI (Type 1) Route for ESI 0:2:2:2:2:2:2:2:2, RT for EVI, ETID 1, Label 200, P = 1, V = 01, M = 10
2

## Slide 42: L2VPN and ECMP That weird thing and its solution

## Slide 43: Hashing theory
By default IP read after labels with modern hardware (L3VPN, Type 5 EVPN)
Challenge with L2 encapsulated packets (PWE, Type 2 EVPN, VPWS)
In case Flow-labels like FAT&Entropy, override any IP header
Summary
  L2 encapsulated services can benefit regards flow-labels
  IP encapsulated services, no need with most modern implementations

## Slide 44: L3VPN without flow label
P2
Po1
PE1
CE-1
P1
PE2
CE-2
C-Tag 512
MPLS Transport PUSH 10000
IP/TCP
Flow#1 99.99.99.1 > 77.77.77.1 TCP 5901
Flow#2 99.9.9.1 > 77.7.7.1 TCP 5903
MPLS ELI PUSH 7
e15
LAG
ECMP SCENARIO MPLS
e13
C-Tag 512
MPLS Transport PUSH 10000
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS Transport 10000
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS Transport POP
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
e3
P Core unaware other than more labelstack Perfect ECMP for LAG members (e13,15)
qumran-ovre-p2(config)#watch 3 sh interface counters rate | nz
Every 3.0s: CliShell -s ar -p 15 -c sh interface counters rate | nz
Port Name Intvl In Mbps % In Kpps Out Mbps % Out Kpps
Et3 0:05 24.2 2.5% 5 1.5 0.2% 2
Et13 5:00 0.8 0.1% 1 12.9 1.3% 2
Et15 5:00 0.8 0.1% 1 11.3 1.2% 2
Po1 5:00 1.6 0.1% 2 24.2 1.2% 4
(…)
Notes: TE

## Slide 45: L3VPN with flow label
P2
Po1
PE1
CE-1
P1
PE2
CE-2
C-Tag 512
MPLS Transport PUSH 10000
IP/TCP
Flow#1 99.99.99.1 > 77.77.77.1 TCP 5901
Flow#2 99.9.9.1 > 77.7.7.1 TCP 5903
MPLS ELI PUSH 7
e15
LAG
ECMP SCENARIO MPLS
e13
C-Tag 512
MPLS Transport PUSH 10000
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS Transport 10000
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS Transport POP
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
qumran-ovre-p2(config)#watch 2 sh interface counters rate | nz
Every 2.0s: CliShell -s ar -p 15 -c sh interface counters rate | nz
Port Name Intvl In Mbps % In Kpps Out Mbps % Out Kpps
Et3 0:05 23.9 2.5% 4 1.5 0.2% 2
Et13 5:00 0.8 0.1% 1 12.0 1.2% 2
Et15 5:00 0.8 0.1% 1 12.4 1.3% 2
Po1 5:00 1.6 0.1% 2 24.5 1.3% 5
(…)
e3
P Core unaware other than more labelstack Perfect ECMP for LAG members (e13,15)
Notes: TE

## Slide 46: L2VPN without flow label
P2
P1
PE2
C-Tag 512
C-Tag 512
MPLS Transport PUSH 10000
IP/TCP
Flow#1 88.88.88.8 > 88.88.88.1 TCP 5900
Flow#2 88.8.8.8 > 88.8.8.1 TCP 5902
MAC
00:1c:73:21:11:4a > 00:1c:73:68:59:a7
MPLS ELI PUSH 7
MPLS VPN 17
LAG
ECMP SCENARIO MPLS
C-Tag 512
C-Tag 512
MPLS Transport PUSH 10000
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
C-Tag 512
MPLS Transport 10000
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS Transport POP
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
qumran-ovre-p2#watch 2 sh interface counters rate | nz
Every 2.0s: CliShell -s ar -p 15 -c sh interface counters rate | nz
Port Name Intvl In Mbps % In Kpps Out Mbps % Out Kpps
Et3 0:05 25.0 2.6% 5 1.9 0.2% 2
Et13 5:00 2.0 0.2% 2 24.8 2.6% 4
Po1 5:00 2.0 0.1% 2 24.8 1.3% 4
(…)
P2
Po1
PE1
CE-1
P1
PE2
CE-2
e15
e13
e3
P Core unaware other than more labelstack No ECMP for LAG members (e13,15)
Notes: TE

## Slide 47: L2VPN with flow label
P2
P1
PE2
C-Tag 512
C-Tag 512
MPLS Transport PUSH 10000
IP/TCP
Flow#1 88.88.88.8 > 88.88.88.1 TCP 5900
Flow#2 88.8.8.8 > 88.8.8.1 TCP 5902
MAC
00:1c:73:21:11:4a > 00:1c:73:68:59:a7
MPLS ELI PUSH 7
MPLS VPN 17
LAG
ECMP SCENARIO MPLS
C-Tag 512
C-Tag 512
MPLS Transport PUSH 10000
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
C-Tag 512
MPLS Transport 10000
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS Transport POP
MPLS ELI 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
C-Tag 512
MPLS ELI PUSH 7
MPLS EL (Flow#1) (Flow#2)
MPLS VPN 17
qumran-ovre-p2#watch 2 sh interface counters rate | nz
Every 2.0s: CliShell -s ar -p 15 -c sh interface counters rate | nz
Port Name Intvl In Mbps % In Kpps Out Mbps % Out Kpps
Et3 0:05 25.5 2.6% 5 2.0 0.2% 2
Et13 5:00 0.8 0.1% 0 12.5 1.3% 2
Et15 5:00 1.3 0.2% 1 12.6 1.3% 2
Po1 5:00 2.1 0.1% 2 25.1 1.3% 5
(…)
P2
Po1
PE1
CE-1
P1
PE2
CE-2
e15
e13
e3
P Core unaware other than more labelstack Perfect ECMP for LAG members (e13,15)
Notes: TE

## Slide 48: Flows with Entropy header
[lunkan@qumran-ovre-p2 ~]$ tcpdump -i mirror0 -nn -q mpls -c 10 | grep 100000
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on mirror0, link-type EN10MB (Ethernet), capture size 262144 bytes
(…)
13:01:44.092529 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.092532 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.093003 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.093006 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.093399 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.093402 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.093805 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.093809 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.094201 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.094205 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.094595 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 329666, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
(…)
13:01:44.103867 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103870 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103873 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103892 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103895 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103910 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103943 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103946 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103949 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103952 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
13:01:44.103968 a8:d0:e5:5d:37:60 > 28:99:3a:06:37:23, MPLS unicast, length 624: MPLS (label 100000, exp 0, ttl 255) (label 7, exp 0, ttl 255) (label 486732, exp 0, ttl 0) (label 17, exp 0, [S], ttl 255)
(…)
Outerlabel 100000, ELI 7, EL 329666/486732 and Innerlabel (VPN) 17 (S-bit set)
Only Entropy labels (EL) between Outerlabel and Innerlabel are unique for the flows
Entopy label indicator (ELI)
Entopy label (EL)
Notes: TE

## Slide 49: Details ELI/EL header
(…)
Ethernet II, Src: a8:d0:e5:5d:37:60, Dst: 28:99:3a:06:37:23
(…)
MultiProtocol Label Switching Header, Label: 100000, Exp: 0, S: 0, TTL: 255
0001 1000 0110 1010 0000 .... .... .... = MPLS Label: 100000
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
MultiProtocol Label Switching Header, Label: 7 (Entropy Label Indicator (ELI)), Exp: 0, S: 0, TTL: 255
0000 0000 0000 0000 0111 .... .... .... = MPLS Label: Entropy Label Indicator (ELI) (7)
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
MultiProtocol Label Switching Header, Label: 975710, Exp: 0, S: 0, TTL: 0
1110 1110 0011 0101 1110 .... .... .... = MPLS Label: 975710
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 0000 0000 = MPLS TTL: 0
MultiProtocol Label Switching Header, Label: 17, Exp: 0, S: 1, TTL: 255
0000 0000 0000 0001 0001 .... .... .... = MPLS Label: 17
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...1 .... .... = MPLS Bottom Of Label Stack: 1
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
(...)
Ethernet II, Src: 00:1c:73:21:11:4a, Dst: 00:1c:73:68:59:a7
(…)
802.1Q Virtual LAN, PRI: 0, DEI: 0, ID: 512
(…)
Internet Protocol Version 4, Src: 88.88.88.8, Dst: 88.88.88.1
(...)
Transmission Control Protocol, Src Port: 45714, Dst Port: 5900, Seq: 96417, Ack: 1, Len: 524
(…)
(…)
Ethernet II, Src: a8:d0:e5:5d:37:60, Dst: 28:99:3a:06:37:23
(…)
MultiProtocol Label Switching Header, Label: 100000, Exp: 0, S: 0, TTL: 255
0001 1000 0110 1010 0000 .... .... .... = MPLS Label: 100000
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
MultiProtocol Label Switching Header, Label: 7 (Entropy Label Indicator (ELI)), Exp: 0, S: 0, TTL: 255
0000 0000 0000 0000 0111 .... .... .... = MPLS Label: Entropy Label Indicator (ELI) (7)
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
MultiProtocol Label Switching Header, Label: 735042, Exp: 0, S: 0, TTL: 0
1011 0011 0111 0100 0010 .... .... .... = MPLS Label: 735042
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 0000 0000 = MPLS TTL: 0
MultiProtocol Label Switching Header, Label: 17, Exp: 0, S: 1, TTL: 255
0000 0000 0000 0001 0001 .... .... .... = MPLS Label: 17
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...1 .... .... = MPLS Bottom Of Label Stack: 1
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
(...)
Ethernet II, Src: 00:1c:73:21:11:4a, Dst: 00:1c:73:68:59:a7
(…)
802.1Q Virtual LAN, PRI: 0, DEI: 0, ID: 512
(…)
Internet Protocol Version 4, Src: 88.8.8.8, Dst: 88.8.8.1
(...)
Transmission Control Protocol, Src Port: 45902, Dst Port: 5902, Seq: 34061, Ack: 1, Len: 524
(...)
Notes: TE

## Slide 50: Flows with Fat label
[lunkan@qumran-under-p1 ~]$ tcpdump -i mirror0 -nn -q mpls
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on mirror0, link-type EN10MB (Ethernet), capture size 262144 bytes
15:50:44.873774 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 136: MPLS (label 100001, exp 1, ttl 255) (label 109, exp 0, [S], ttl 0)
15:50:44.873906 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 136: MPLS (label 100001, exp 0, ttl 255) (label 19, exp 0, [S], ttl 0)
15:50:44.874067 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 136: MPLS (label 100001, exp 1, ttl 255) (label 109, exp 0, [S], ttl 0)
15:50:44.874175 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 136: MPLS (label 100001, exp 0, ttl 255) (label 19, exp 0, [S], ttl 0)
15:50:44.874284 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 136: MPLS (label 100001, exp 1, ttl 255) (label 109, exp 0, [S], ttl 0)
15:50:44.874387 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 136: MPLS (label 100001, exp 0, ttl 255) (label 19, exp 0, [S], ttl 0)
15:50:44.874534 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 136: MPLS (label 100001, exp 1, ttl 255) (label 109, exp 0, [S], ttl 0)
15:50:44.874632 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 136: MPLS (label 100001, exp 0, ttl 255) (label 19, exp 0, [S], ttl 0)
15:50:44.874714 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 136: MPLS (label 100001, exp 1, ttl 255) (label 109, exp 0, [S], ttl 0)
15:50:44.874813 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 136: MPLS (label 100001, exp 0, ttl 255) (label 19, exp 0, [S], ttl 0)
(…)
15:50:46.219130 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 156: MPLS (label 100001, exp 1, ttl 255) (label 182, exp 0, [S], ttl 0)
15:50:46.219192 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 156: MPLS (label 100001, exp 0, ttl 255) (label 192, exp 0, [S], ttl 0)
15:50:46.219402 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 156: MPLS (label 100001, exp 1, ttl 255) (label 182, exp 0, [S], ttl 0)
15:50:46.219502 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 156: MPLS (label 100001, exp 0, ttl 255) (label 192, exp 0, [S], ttl 0)
15:50:46.219578 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 156: MPLS (label 100001, exp 1, ttl 255) (label 182, exp 0, [S], ttl 0)
15:50:46.219675 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 156: MPLS (label 100001, exp 0, ttl 255) (label 192, exp 0, [S], ttl 0)
15:50:46.219746 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 156: MPLS (label 100001, exp 1, ttl 255) (label 182, exp 0, [S], ttl 0)
15:50:46.219855 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 156: MPLS (label 100001, exp 0, ttl 255) (label 192, exp 0, [S], ttl 0)
15:50:46.219927 28:99:3a:d1:93:8a > 28:99:3a:06:37:23, MPLS unicast, length 156: MPLS (label 100001, exp 1, ttl 255) (label 182, exp 0, [S], ttl 0)
15:50:46.220025 28:99:3a:06:37:23 > 28:99:3a:d1:93:8a, MPLS unicast, length 156: MPLS (label 100001, exp 0, ttl 255) (label 192, exp 0, [S], ttl 0))
^C
Inner label (VC) 100001
The flow labels with S-bit set (bottom of stack) are related to the sessions
IPv4 PING (109,19 and IPv6 (182,192)
Notes: TE

## Slide 51: Details Fat label
Ethernet II, Src: 28:99:3a:d1:93:8a, Dst: 28:e 99:3a:06:37:23
Type: MPLS label switched packet (0x8847)
(…)
MultiProtocol Label Switching Header, Label: 100001, Exp: 1, S: 0, TTL: 255
0001 1000 0110 1010 0001 .... .... .... = MPLS Label: 100001
.... .... .... .... .... 001. .... .... = MPLS Experimental Bits: 1
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
MultiProtocol Label Switching Header, Label: 109, Exp: 0, S: 1, TTL: 0
0000 0000 0000 0110 1101 .... .... .... = MPLS Label: 109
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...1 .... .... = MPLS Bottom Of Label Stack: 1
.... .... .... .... .... .... 0000 0000 = MPLS TTL: 0
Ethernet II, Src: 00:1c:73:21:11:4a, Dst: 00:1c:73:68:59:a7
Type: IPv4 (0x0800)
(…)
Internet Protocol Version 4, Src: 4.0.0.1, Dst: 4.0.0.2
Protocol: ICMP (1)
(…)
Internet Control Message Protocol
Type: 8 (Echo (ping) request)
Code: 0
Checksum: 0x1ee7 [correct]
[Checksum Status: Good]
Identifier (BE): 490 (0x01ea)
Identifier (LE): 59905 (0xea01)
Sequence number (BE): 1 (0x0001)
Sequence number (LE): 256 (0x0100)
Timestamp from icmp data: Feb 17, 2020 17:02:32.070030000 CET
[Timestamp from icmp data (relative): 331.477788000 seconds]
Data (64 bytes)
Ethernet II, Src: 28:99:3a:d1:93:8a, Dst: 28:99:3a:06:37:23
Type: MPLS label switched packet (0x8847)
(…)
MultiProtocol Label Switching Header, Label: 100001, Exp: 1, S: 0, TTL: 255
0001 1000 0110 1010 0001 .... .... .... = MPLS Label: 100001
.... .... .... .... .... 001. .... .... = MPLS Experimental Bits: 1
.... .... .... .... .... ...0 .... .... = MPLS Bottom Of Label Stack: 0
.... .... .... .... .... .... 1111 1111 = MPLS TTL: 255
MultiProtocol Label Switching Header, Label: 182, Exp: 0, S: 1, TTL: 0
0000 0000 0000 1011 0110 .... .... .... = MPLS Label: 182
.... .... .... .... .... 000. .... .... = MPLS Experimental Bits: 0
.... .... .... .... .... ...1 .... .... = MPLS Bottom Of Label Stack: 1
.... .... .... .... .... .... 0000 0000 = MPLS TTL: 0
Ethernet II, Src: 00:1c:73:21:11:4a, Dst: 00:1c:73:68:59:a7
Type: IPv6 (0x86dd)
(…)
Internet Protocol Version 6, Src: fd00:4::1, Dst: fd00:4::2
Next Header: ICMPv6 (58)
(…)
Internet Control Message Protocol v6
Type: Echo (ping) request (128)
Code: 0
Checksum: 0x4d2f [correct]
[Checksum Status: Good]
Identifier: 0x01ee
Sequence: 1
Data (72 bytes)
IPv4
IPv6
Notes: TE

## Slide 52: Route resolution
Default
112.112.0.1/32
Multiple ways
  LDP
  ISIS-SR
  BGP-SR
But why not just IP ?
PE2
112.112.112.112/32
iBGP
EVPN_1
62.0.0.0/24
qumran-under-p1(config-tunnel-rib-peter)#sh ip ro vrf evpn_1 62.0.0.0/24
VRF: evpn_1
(…)
B I 62.0.0.0/24 [200/0] via 112.112.112.112/32, LDP tunnel index 1, label 132891
via 1.1.1.3, Ethernet1, label imp-null(3)
(…)
B I 62.0.0.0/24 [200/0] via 112.112.112.112/32, IS-IS SR tunnel index 1, label 132891
via 1.1.1.3, Ethernet1, label imp-null(3)
(…)
B I 62.0.0.0/24 [200/0] via 112.112.112.112/32, BGP LU tunnel index 21, label 132891
via 1.1.1.3, Ethernet1, label imp-null(3)
bgp-edge2(config)#sh ip ro vrf evpn_1 bgp
VRF: evpn_1
(…)
B I 62.0.0.0/24 [200/0] via VTEP 112.112.112.112 VNI 10 router-mac 28:99:3a:06:37:23
ISIS-SR
LDP
BGP-LU/SR
PE1
1111.111.111.111/32

## Slide 53: EVPN VPWS Sample PW => VPWS

## Slide 54: E-Line PW Sample
LDP Based Pseudowire (PW)
RFC 4447
Two types
  Type 4 (VLAN Type)
  Type 5 (Port Type)
  Here L2 Subinterface
!
interface Ethernet23
description trunk to t3 e3
load-interval 5
mtu 9000
no switchport
!
interface Ethernet23.101
description PWE subinterface VLAN 101 to ce t3 e3
encapsulation dot1q vlan 101
!
mpls ip
!
mpls ldp
router-id 112.112.112.112
transport-address interface Loopback0
neighbor 111.111.111.111 targeted
interface disabled default
no shutdown
!
pseudowires
pseudowire pwe1
neighbor 111.111.111.111
pseudowire-id 1
mtu 9000
control-word
label flow
!
!
patch panel
patch e23sub101pwe
shutdown
connector 1 interface Ethernet23.101
connector 2 pseudowire ldp pwe1
!
!

## Slide 55: E-Line PW Sample…
LDP Based Pseudowire (PW)
RFC 4447
Two types
  Type 4 (VLAN Type)
  Type 5 (Port Type)
  Here L2 Subinterface
qumran-ovre-p2(config-patch)#sh patch panel e23sub101pwe detail
PW Fault Legend:
ET-IN - Ethernet receive fault
ET-OUT - Ethernet transmit fault
TUN-IN - Tunnel receive fault
TUN-OUT - Tunnel transmit fault
NF - Pseudowire not forwarding (other reason)
Patch: e23sub101pwe, Status: Up
Connector 1: Ethernet23.101
Status: Up
Connector 2: LDP neighbor 111.111.111.111 PW ID 1
Status: Up
Local MPLS label: 100002, Group ID: 0x0
MTU: 9000, 802.1Q VLAN request sent: -
Flow label capability: transmit and receive
Supported VCCV CV types: LSP ping
Supported VCCV CC types: Router alert label
Neighbor MPLS label: 100002, Group ID: 0x0
MTU: 9000, 802.1Q VLAN request received: -
Flow label capability: transmit and receive
Supported VCCV CV types: LSP ping
Supported VCCV CC types: Router alert label
PW type: 5 (raw), Control word: Y
Flow label used: transmitted and received
Tunnel type: LDP, Tunnel index: 2

## Slide 56: E-Line VPWS Sample
BGP Based VPWS
No changes regards existing interface configuration
Add to your probably already existing BGP stanza
  BGP Peer/RR for autodiscovery
  RD and Route-target Adj-RIB-In/Out policy
  Pseudowire id
Change VC from LDP BGP VPWS pseudowire
!
router bgp 65000
router-id 112.112.112.112
bgp transport pmtud
maximum-paths 2 ecmp 2
neighbor 65000 peer group
neighbor 65000 remote-as 65000
neighbor 65000 update-source Loopback0
neighbor 65000 additional-paths send any
neighbor 65000 route-map whatever out
neighbor 65000 send-community standard extended large
neighbor 65000 maximum-routes 0
neighbor 111.111.111.111 peer group 65000
neighbor 2001:1:1:1::2 peer group 65000
redistribute connected
!
vpws vpws101
rd 112.112.112.112:101
route-target import evpn 65000:101
route-target export evpn 65000:101
mpls control-word
mtu 9000
!
pseudowire pwe101
evpn vpws id local 112 remote 111
!
address-family evpn
neighbor default encapsulation mpls next-hop-self source-interface Loopback0
next-hop mpls resolution ribs tunnel-rib peter
neighbor 65000 activate
!
!
patch panel
patch e23sub101pwe
shutdown
connector 1 interface Ethernet23.101
connector 2 pseudowire ldp pwe1
!
patch e23sub101vpws
connector 1 interface Ethernet23.101
connector 2 pseudowire bgp vpws vpws101 pseudowire pwe101
(…)

## Slide 57: E-Line VPWS Sample…
qumran-ovre-p2(config-router-bgp)#sh pa panel e23sub101vpws detail
PW Fault Legend:
ET-IN - Ethernet receive fault
ET-OUT - Ethernet transmit fault
TUN-IN - Tunnel receive fault
TUN-OUT - Tunnel transmit fault
NF - Pseudowire not forwarding (other reason)
Patch: e23sub101vpws, Status: Up
Connector 1: Ethernet23.101
Status: Up
Connector 2: BGP VPWS vpws101 Pseudowire pwe101
Status: Up
Local MPLS label: 100001
MTU: 9000, Control word: Y
Neighbor 111.111.111.111, MPLS label: 100001
Tunnel type: IS-IS SR IPv4, Tunnel index: 3
MTU: 9000, Control word: Y
EVPN VPWS type: VLAN-based
BGP Based VPWS
No changes regards existing interface configuration
Add to your probably already existing BGP stanza
  BGP Peer/RR for autodiscovery
  RD and Route-target Adj-RIB-In/Out policy
  Pseudowire id
Change VC from LDP BGP VPWS pseudowire